## Slide 1: Electrical Resistivity Tomography Technical Overview
July 15, 2025, Online
Lena Schwebs, University of Wyoming

## Slide 2: Webinar Outline
ERT Applications
ERT Physics and Resistivity of Soils and Rocks
Field Measurements
Geophysical Inversion

## Slide 3: Animation: Electrical Resistivity Tomography

## Slide 4: Near-surface ERT Applications
Groundwater exploration
Saltwater intrusions
Agriculture: soil moisture and root zone
Soil/groundwater contaminant mapping
Landfill monitoring
Snowmelt/hillslope dynamics
Watlet et al. (2018)
Notes: Top image: Changes in resistivity over time for several winter wheat varieties along a 30m transect. The variety names are shown in third image.
Bottom image: internal survey of a dam
Expand on your explanations for each application (Beth: looks like DeeDee proposed removing ~4 slides at this point)

## Slide 5: Near-surface ERT Applications
Groundwater exploration
Saltwater intrusions
Agriculture: soil moisture and root zone
Soil/groundwater contaminant mapping
Landfill monitoring
Snowmelt/hillslope dynamics
Goebel et al. (2017)
Notes: ERT cross sections along the coast where red indicates salt water intrusions due to the very low resistivity. The sporadic pattern of the saltwater intrusions also demonstrate the advantage ERT has in monitoring on a plot scale rather than point sources like wells along the coast.

## Slide 6: Near-surface ERT Applications
Groundwater exploration
Saltwater intrusions
Agriculture: soil moisture and root zone
Soil/groundwater contaminant mapping
Landfill monitoring
Snowmelt/hillslope dynamics
Whalley et al. (2017)
Notes: Changes in resistivity over time for several winter wheat varieties. Notice how the higher resistivity (red) section change for each wheat variety.

## Slide 7: Near-surface ERT Applications
Groundwater exploration
Saltwater intrusions
Agriculture: soil moisture and root zone
Soil/groundwater contaminant mapping
Landfill monitoring
Snowmelt/hillslope dynamics
Thayer et al. (2018)
Notes: Top image: Changes in resistivity over time for several winter wheat varieties along a 30m transect. The variety names are shown in third image.
Bottom image: internal survey of a dam
Expand on your explanations for each application (Beth: looks like DeeDee proposed removing ~4 slides at this point)

## Slide 8: Electricity concepts review:
Voltage (V or ΔV): “potential difference” the amount of potential energy electrons have in a circuit [volts]
Current (I): The amount of electricity that is flowing; the number of electrons moving through a circuit per unit of time [Amperes]
Resistance (R): how much the material that current is moving through opposes the flow of electrons [Ohms]

## Slide 9: Electricity concepts review:
Voltage (V or ΔV): “potential difference” the amount of potential energy electrons have in a circuit [volts]
Current (I): The amount of electricity that is flowing; the number of electrons moving through a circuit per unit of time [Amperes]
Resistance (R): how much the material that current is moving through opposes the flow of electrons [Ohms]
Ohm’s Law:

## Slide 10: Resistivity (ρ) vs. resistance (R)
resistivity
resistance
From Unit 2
Geometric factor
One-dimensional (1D) current flow in a column
Relationship between resistivity (intrinsic/physical property) and resistance (what we can measure) for one-dimensional current flow
Notes: Resistivity is the reciprocal of conductivity
Both are fundamental properties of a material
Where resistivity is how difficult it is for electric current to flow in a material and conductivity is how easy
Both properties are plotted throughout the modules so it’s important to check what is plotted in each image

## Slide 11: Resistivity (ρ) vs. conductivity (σ)
resistivity
how difficult it is for electric current to flow in a material
conductivity
how easy it is for electric current to flow in a material
From Unit 2
Notes: Resistivity is the reciprocal of conductivity
Both are fundamental properties of a material
Where resistivity is how difficult it is for electric current to flow in a material and conductivity is how easy
Both properties are plotted throughout the modules so it’s important to check what is plotted in each image

## Slide 12: What is ERT?
Based on Ohm’s law:
Put electrodes into the ground and measure potential difference (voltage)
Transfer resistance:
From Unit 3
Notes: Explain basics:
I= current – flow of electricity
v = Voltage - pressure that pushes this current
R= resistance - properties of the material that slows the current.
Transfer Resistance is what we measure
So we inject a known current, measure the voltage, and calculate resistance from Ohm’s Law to get what we call our measured transfer resistance

## Slide 13: Electrical resistivity imaging
electrodes
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press
From Unit 3
Notes: We typically collect 2D or 3D surveys
  2D is a single line
  3D is imaged on slide
You can have 10s to 100s of electrodes spaced at custom increments
  For teaching and a pretty standard survey would be would be 28-56 electrodes spaced 1-2m
The depth of investigation depends on the subsurface, but we typically expect the depth to be 10-20% of the survey line

## Slide 14: Transfer resistances and Apparent resistivity
Apparent resistivity:
the resistivity of a homogenous subsurface that the measured voltage and current are equivalent to
Transfer resistance with units of ohms
is a function of the intrinsic resistivity of the subsurface which depends on the sensitivity of the array
From Unit 3
Notes: transfer resistance, is measured with a resistivity imaging instrument.
When the transfer resistance is multiplied by the geometric factor for the specific array used, the apparent resistivity is calculated.
This is generally a complex function of the unknown true resistivity structure of the subsurface.
The value of the apparent resistivity will depend on the sensitivity of the array being use

## Slide 15: Transfer resistances and Apparent resistivity
Apparent resistivity:
the resistivity of a homogenous subsurface that the measured voltage and current are equivalent to
Transfer resistance with units of ohms
Geometric factor
K is a function of distance between electrodes:
farther apart = deeper current lines
From Unit 3
is a function of the intrinsic resistivity of the subsurface which depends on the sensitivity of the array
Notes: The geometric factor of the array is given by this equation,
The geometric factor is used to calculate the apparent resistivity based from the measured transfer resistance.
but you just need to know it’s a function of the distance between the electrodes and the instrument will calculate it for you.
Apparent resistivity is NOT the true resistivity of the subsurface. Apparent res does not account for the geometry of the subsurface  inversion takes care of this, more later

## Slide 16: Standard electrode configurations
Schlumberger
Wenner
Dipole-Dipole
Notes: There are different sensitivities w different arrays
Advantages and disadvantages for each array
Explain S/N and Speed
Speed factors:
  Array
  Injection time
  # of measurements
  Stacking #
  Contact res (does it have to keep trying?)
  Reciprocals
Dipole-dipole can take X measurements at once but Wenner and Schlumberger are 1 measurement at a time
Some are better w lateral and others are better w vertical

## Slide 17: Resistivity of geomaterials
Notes: Resistivity of geomaterials can be complex with a lot of overlap and dependence on saturation
Highlight ground water and sea water
Also the subsurface is typically composed of multiple materials with overlapping resistivities so it’s important to know about the geology of your field site
Image: https://em.geosci.xyz/content/physical_properties/electrical_conductivity/electrical_conductivity_values.html

## Slide 18: What affects the resistivity and conductivity of geomaterials?
Effect | Resistivity | Conductivity
Increasing porosity | ↓ | ↑
Increasing pore fluid salinity | ↓ | ↑
Increasing surface conductance | ↓ | ↑
Increasing connectedness/connectivity | ↓ | ↑
Increasing saturation | ↓ | ↑
Weathering | ↓ | ↑
Compaction | ↑ | ↓
Increasing formation factor | ↑ | ↓
Increasing tortuosity | ↑ | ↓
Images from Unit 2: Geophysical Properties of the Subsurface
Notes: Various processes that affect conductivity and resistivity of geomaterials
There is a lot of overlap between these processes
  Ex: Increased weathering typically leads to increased porosity, connectedness/connectivity, and decreasing tortuosity, and decreasing formation factor
Top image: less vs more tortuous/connected
Bottom image: less saturation leads to less connectivity and more tortuosity
(New slide: best added to Unit 2 Introduction to resistivity in soils and rocks as supplemental slides)
Glover, P. W. J. (2015). Geophysical Properties of the Near Surface Earth: Electrical Properties.

## Slide 19: Field Survey Design Basics
Array (Wenner, Dipole-Dipole)
  Vertical vs lateral sensitivity?
  Signal to noise ratio?
  How much time do you have?
Electrode spacing
  What resolution do you want?
  How deep are you trying to measure/how long of a line do you need?
    Depth of investigation is approximately 10-20% of the length of the line
Stacks
  How many times do you want to repeat individual measurements
  Data quality vs time of survey

## Slide 20: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 21: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
  A1: Dipole-dipole for better lateral sensitivity
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 22: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
  A1: Dipole-dipole for better lateral sensitivity
Q2: What should be the minimum line length?
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 23: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
  A1: Dipole-dipole for better lateral sensitivity
Q2: What should be the minimum line length?
  A2: 10m = 0.1*Line length  Line length = 100m
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 24: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
  A1: Dipole-dipole for better lateral sensitivity
Q2: What should be the minimum line length?
  A2: 10m = 0.1*Line length  Line length = 100m
Q3: If you have 56 electrodes, what would be a good electrode spacing to reach the line length in Q2?
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 25: Design your own survey
ERT Target:
Magmatic dike in sandstone
Beginning at ~10m depth
Questions:
Q1: What array would be best?
  A1: Dipole-dipole for better lateral sensitivity
Q2: What should be the minimum line length?
  A2: 10m = 0.1*Line length  Line length = 100m
Q3: If you have 56 electrodes, what would be a good electrode spacing to reach the line length in Q2?
  A3: 2m spacing
Answer in the Chat
Notes: Array: Dipole-dipole because of lateral resolution
Line length: 50-100m
Electrode separation: No more than 20m
I think it would be helpful to add something about survey design – Image-able depth from given line length
– Resolvable features with different electrode spacing
Then perhaps you could pose a question or two related to survey design decisions OR changes that you might see given a certain subsurface change (ex. clay-filled cracks vs air-filled)

## Slide 26: Field Equipment at the Workshop
AGI SuperSting Resistivity Meter
Electrodes and Cables
Resistivity Meter
Image Sources: AGI USA
Switchbox

## Slide 27
Line workers
Laying out the line
electrodes
From Unit 3
Notes: At the field site, a lot of work goes into setting up the survey
First you set up a tape measure of your survey line
  You want this as straight as possible!!
  Hard to do for long lines
  Even harder with trees and such
Hammer in electrodes at designated spots (remember electrode 1 is at 0m)
Lay out the cable with the correct takeout at the correct electrodes and connect them

## Slide 28: Electrical resistivity imaging
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press
96 electrodes spaced 1.5 m apart
Line length: 142.5 m
Time to setup: 1 hr. and 30 mins with team of 5
Completed line
From Unit 3
electrodes
Notes: Compare schematic to field site

## Slide 29
Contact resistance check
Voltage and current levels (change settings?)
System checks
From Unit 3
Notes: Once the line is set up, the instrument can be connected and settings changed
Contact resistance check

## Slide 30
It’s not working!!
This electrode isn’t connected!
I’ll fix it!!
Dum-de-dum..
Fixing problems
From Unit 3
Notes: Problem-solving
Fix electrodes that don’t have good contact or are disconnected
What is good contact resistance?
  2-3k Ohm is suggested by manufacturers
  Realistic for wet climates
  What about dry arid?
  We aim for about 10kOhm but less than 20kOhm is okay

## Slide 31
Waiting for data to be acquired
Expert(?)
Engaged students
From Unit 3
Notes: Start survey
It can take hours. Depends on:
  Array
  Injection time
  Reciprocals
  Stacks/Max stacks
  Number of electrodes
Good time to talk to students or set up seismic!
Don’t need these slides – they’re not setting it up today

## Slide 32
Packing up the line
From Unit 3
Notes: Once the survey finishes measuring, time to pack up line
Tape measure should be last thing you take down to remember where all the electrodes are supposed to be
I think the main point for slides 17-20 is a teaser about what they can encounter in the field (esp a view of the field that has higher grass than campus)

## Slide 33: What is inverse modeling?
The process by which the transfer resistance or apparent resistivity measurements acquired from the surface are transformed into estimated images of the subsurface resistivity (or conductivity)
ρa (Ωm)
n=1
n=5
n=10
log10 (resistivity in Ωm)
Forward
modeling
Inverse
modeling
Pseudo section
Resistivity distribution
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and applications to the near-surface Earth, In Press
From Unit 4: The Magic of Geophysical Inversion
Notes: Don’t need too much since you’ll be going over this during the workshop.

## Slide 34: Inversion: a pair of fuzzy glasses
S
Note: There is NO such thing as geophysical X-ray vision! No silver bullets!
G
Inversion of resistivity data is not like donning a pair of x-ray glasses
The fuzzy, indirect information obtained from electrical resistivity inversion should always be interpreted in conjunction with other available datasets.
Image courtesy of Fred Day-Lewis (USGS)
From Unit 4

## Slide 35: ResIPy Processing Workflow
Load/visualize raw data
Preprocess data
Build mesh grid for model
Interpret final model

## Slide 36: Measurement error
V
I
A
B
N
M
Normal measurement
V
I
A
B
N
M
Reciprocal measurement
switched
Reciprocal error: the difference between the normal measurement and the reciprocal measurement
Theoretically, the two measurements should be the same
Requires double the measurements and therefore double the time
From Unit 4
Notes: A robust way to assess the errors in the measurements. The theory of reciprocity states that the normal and reciprocal measurement must have the same resistance (and hence apparent resistivity).
Differences between the two measurements quantify the errors
Better assessment of data quality → can account for repeated errors that stacking errors do not
Double the measurements = double the time → think of wenner vs dipole-dipole
Do you think it is helpful to getting these details now OR would it be better during the data processing part?
Maybe fewer slides?
What are the more important elements for them to know ahead of time about processing?
--inversion involves an iterative process
--there are ways to quantify the errors

## Slide 37: What do images mean?
Infer spatial variation in soil/rock type, chemistry of the fluids in the ground, water content……..
Increasing conductivity – what does it mean?
Increasing salinity of water in soils?
Increasing water content?
Increase in porosity?
Increase in fine-grained sediments?
Image of subsurface electrical conductivity from the Harrier Meadow survey
From Unit 4
Notes: But what do these images really mean?
Unit 2 covers the relationships between the electrical conductivity of soils and the physical and chemical properties of soils.
Using Archie’s Laws, we learned that electrical conductivity increases with the salinity of the pore fluids, the porosity of the soil and the water content if the soil is not saturated.
We also learned that fine grained materials such as clays also increase electrical conductivity. The changes in conductivity observed with electrical imaging result from changes in such factors.
At Harrier Meadow we know that the soils are saturated beneath the top 20 cm so the changes in conductivity in this image most likely represent changes in salinity and/or changes in soil type.
Distinguishing between such effects is best done using some direct sampling at a few locations – indeed, the interpretation of geophysical datasets is always improved with some direct observations.
We will use some direct measurements to explore the significance of these conductivity images further in Unit 5.

## Slide 38: Thank you! Questions?
Image of subsurface electrical conductivity from the Harrier Meadow survey

## Slide 39: Supplementary Slides

## Slide 40: Standard electrode configurations
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press
The instrument calculates K for you.
Specific array types are used with easy
to compute geometric factors (K) – (K depends on array)
Wenner array:
Dipole-dipole array:
From Unit 3
Notes: Partly because the general geometric factor for a 4 electrode array is a bit of a mouthful, geophysicists have adopted the use of standard arrays that yield a simpler expression of the geometric factor.
We will work with the Wenner array where the geometric factor is simply 2 times pi times the electrode spacing a.
We will also work with the dipole-dipole array. The geometric factor for the dipole-dipole array is a bit more involved but is again determined by a constant electrode spacing, and also an integer n representing the multiplier on a that defines the spacing between current electrode B and potential electrode N.
The other reason that geophysicists use such standard arrays is because they have different sensitivity patterns, meaning that some may be quite good for detecting lateral variations in resistivity whereas others will be good at detecting vertical variations in resistivity.
NOT SURE IF YOU NEED THIS SLIDE

## Slide 41: How does it work?
Synthetic pseudo section
Measured pseudo section (with errors)
Synthetic resistivity model
????
Forward modeling
Statistical comparison
`
UNKNOWN RESISTIVITY MODEL OF THE EARTH
From Unit 4: The Magic of Geophysical Inversion
Notes: Go into this a little – explain it so there’s a transition.

## Slide 42: How does it work?
Synthetic measurements
Field measurements (with errors)
??
Forward modeling
ADEQUATE GOODNESS OF FIT?
NO
Revise synthetic resistivity model
ITERATE
UNKNOWN RESISTIVITY MODEL OF THE EARTH
From Unit 4: The Magic of Geophysical Inversion

## Slide 43: How does it work?
FIELD SUBSURFACE RESISTIVITY ??
Forward modeling
ADEQUATE GOODNESS OF FIT?
YES
Synthetic pseudo section
Measured pseudo section (with errors)
ESTIMATED SUBSURFACE RESISTIVITY MODEL
From Unit 4: The Magic of Geophysical Inversion