## Slide 1
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 2
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 3
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 4
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 5
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 6
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd

## Slide 7
Sample: field notes specific for a resistivity survey
Start=0m on tape
End = 165 m on tape
hillside
Car parked here
N
52 m – depression 3 m wide, 1 m deep
113 m – grass ends, gravel to north
Electrode 1 at x = 0m
Electrode 56 at x = 165m (to northeast)
Electrode spacing = 3m
Start (electrode 1)
296892.6m E
4786704.5 m N
Elevation 1948 m
UTM zone 12
Read with hand-held GPS
WGS84 datum
Azimuth of line N22°E
(line runs SW to NE)
Heading gently uphill
End estimated 5 m higher than start
Issues:
Didn’t get end position because GPS batteries died
Electrodes 23 and 24 wouldn’t work, even after repeated cable & connection checks
Timing:
Batteries on 10:02 a.m. (12. 63V)  Batteries off 11:35 a.m. (12.07 V)
Electrodes watered 10:02-10:25 a.m.
Survey started 10:32 a.m finished 11:15 a.m
Files:
Dipole-dipole geometry, file name sampledd