## Slide 1: Geophysical Interpretation and Comparison with Ground Truthing
Lee Slater
Department of Earth and Environmental Sciences, Rutgers University, Newark, NJ, USA

## Slide 2: Sampling
Setting up the Russian peat corer for sampling at Site 3
Sampled top 0.27-0.48 m of organic sediments that overly gravel fill material

## Slide 3: Retrieved core
Example of organic rich sediments cored at Site 3
Russian peat corer is designed to acquire a well-preserved core of organic rich materials as encountered in wetlands

## Slide 4: Laboratory analysis
Original sample
Dried sample for porosity (f) analysis
Vv = volume of voids
VT = total volume
Sample prepared for particle size analysis
grain size
frequency

## Slide 5: Pore water sampling
Installed a ‘lysimeter’ for acquiring a sample of the fluids in the pores of the organic sediments.
Once equilibrium conditions have returned (after disturbance by the coring) the water from the lysimeter is drained with a pump.
Water in the surrounding pores of the sediment then fills the lysimeter tube and it is subsequently sampled.
Lysimeter installed at Site 4
Water quality probe used to measure salinity of pore fluids

## Slide 6: Our sampling strategy
1
2
3
4
5
6
We sampled six locations based on Layer 1 of the EM inversion as it shows a strong correlation with the pickleweed locations – as you should have discovered in your investigations of the EM data using the story map

## Slide 7: Reinterpreting the resistivity section
Conductivity (mS/m)
organic layer (0.3-0.5 m thick)
contact with hard gravel fill (limit of coring)
?
Notes: Question students – what evidence is there for the organic layer and contact with underlying hard gravel fill? What evidence is there in the resistivity for another contact below the top of the gravel fill?

## Slide 8: Constraining interpretation of EM conductivity images
log10 (conductivity in mS/m)
Layer 1: 0-0.2 m
Layer 2: 0.2-0.5 m
Layer 3: 0.5-0.9 m
Layer 4: 0.9-1.4 m
Layer 5: 1.4-2.1 m
Layer 6: 2.1-3.0 m
Layer 7: below 3.0 m
Questions to consider:
[1] Do the physical and chemical properties measured for the upper organic sediment layer show any correlation with the EM conductivity for the first layer of the inversion?
[2] Is there evidence of a sharp transition to a different layer below 0.3-0.5 m consistent with the gravelly layer encountered in the coring?

## Slide 9: Comparing electrical imaging and EM conductivity mapping
Conductivity (mS/m)
EM inversion is limited to 3 m depth
We cannot see the bottom 2 m of the electrical imaging result in the EM conductivity inversion

## Slide 10: Supporting data summary
 |  |  | Particle size data |  | 
 | Thickness (m) | Porosity* (-) | d10 (mm) | d50 (mm) | Specific conductance (mS/cm)
Site 1 | 0.33 | 0.46 | 5.01 | 70.86 | 20.96
Site 2 | 0.33 | 0.22 | 3.93 | 60.42 | 19.79
Site 3 | 0.43 | 0.23 | 10.25 | 110.99 | 29.32
Site 4 | 0.48 | 0.15 | 4.38 | 113.00 | 29.38
Site 5 | 0.28 | 0.19 | 9.92 | 186.89 | 31.00
Site 6 | 0.27 | 0.18 | 18.27 | 304.97 | 30.20
* assuming a particle density of 1.2 g/cm3
Summary of directly sampled properties of upper organic sediment layer

## Slide 11: Particle size distribution
Determined using a laser particle size analyzer
d10
d50
Increasing surface area
Increasing surface conduction
d50: 50% of sample is finer than this diameter
d10: 10% of sample is finer than this diameter
1
2
3
4
5
6