## Slide 1: A Short Tutorial on Resistivity of Soils and Rocks
Lee Slater
Department of Earth and Environmental Sciences, Rutgers University, Newark, NJ, USA

## Slide 2: Mechanisms of electrical conduction
Electronic conduction in a metal (e.g. in the wiring of a house)
Ionic conduction in a solution (e.g. in soils)

## Slide 3: The electrical property resistivity (ρ) – or conductivity (σ)
resistivity
Fundamental property determining how difficult it is for electric current to flow in a material
conductivity
Fundamental property determining how easy it is for electric current to flow in a material

## Slide 4: Resistivity of earth materials

## Slide 5: What affects the resistivity and conductivity of geomaterials?
Effect | Resistivity | Conductivity
Increasing porosity | ↓ | ↑
Increasing pore fluid salinity | ↓ | ↑
Increasing surface conductance | ↓ | ↑
Increasing connectedness/connectivity | ↓ | ↑
Increasing saturation | ↓ | ↑
Weathering | ↓ | ↑
Compaction | ↑ | ↓
Increasing formation factor | ↑ | ↓
Increasing tortuosity | ↑ | ↓
Images from Unit 2: Geophysical Properties of the Subsurface
Notes: Various processes that affect conductivity and resistivity of geomaterials
There is a lot of overlap between these processes
  Ex: Increased weathering typically leads to increased porosity, connectedness/connectivity, and decreasing tortuosity, and decreasing formation factor
Top image: less vs more tortuous/connected
Bottom image: less saturation leads to less connectivity and more tortuosity
(New slide: best added to Unit 2 Introduction to resistivity in soils and rocks as supplemental slides)
Glover, P. W. J. (2015). Geophysical Properties of the Near Surface Earth: Electrical Properties.

## Slide 6: Ionic conduction in soils
+
-
+
-
ionic fluid
soil (or rock) filled with ionic fluid
Fluid resistivity =
Soil resistivity =
Fluid conductivity (σw) increases with ionic concentration (also with ionic mobility)
F = formation factor
Quantifies how much more resistive the soil is relative to the pore-filling fluid due to the presence of insulating mineral grains
Or how much less conductive it is relative to the pore-filling fluid
Notes: Next let’s consider how ionic conduction in a soil differs from in a fluid.
In a fluid, the conductivity is determined primarily by the concentration of the ions.
In a soil or rock that is fully saturated with a fluid, the resistivity increases due to the presence of the mineral grains, which are assumed to be perfect insulators.
The electrical formation factor is an important property that describes how much more resistive a soil is relative to the fluid that fills its pores.
Alternatively, the electrical formation factor describes how much less conductive the soil is relative to the conductivity of the fluid filling its pores

## Slide 7: Archie’s law
soil (or rock) filled with ionic fluid
Soil resistivity:
Archie’s Law (1942)
interconnected porosity
‘cementation’ exponent
Gustavus E. Archie (1907-1978: Developed petrophysical relationships whilst working for Shell Oil Company
Source: wiki.seg.org
Archie was interested in petroleum reservoirs but his relationships are now also used to explain electrical conduction in soils

## Slide 8: Connectivity in Archie’s law
approximately straight current flow lines
tortuous current flow lines
typically 1.5-2.5 in sandstones
typically 1.1-1.5 in unconsolidated sediments
Archie called m a cementation exponent but we can think about it as a measure of the connectivity of the porosity

## Slide 9: Experimental observations with Archie’s law
Archie’s Law for different values of ‘m’
Fit of Archie’s Law to a sandstone and mixed sandstone/dolomite samples
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 10: Archie’s second law
Undersaturation:
[1] reduces porosity available to conduct current
[2] reduces connectivity
Archie’s 2nd Law (1942)
Sw varies from 0-1
n takes similar values to m
in unconsolidated sediments
Saturated soil
Unsaturated soil

## Slide 11: Form of Archie’s 2nd law
Archie’s 2nd law for different values of the saturation exponent n.
Expressed as a resistivity saturation index Ir (ratio of resistivity of an unsaturated soil to the resistivity at saturation).
Higher values of n reflect poorer connectivity of the pores due to the replacement of water by air

## Slide 12: Surface conduction
Archie’s Law neglects a second pathway for ionic conduction in the electrical double layer (EDL) that forms at the soil mineral-pore fluid interface
This is commonly referred to as surface conduction
Conduction through the pore fluid and along the mineral surface is commonly assumed to be in parallel:
Electrical double layer (EDL)
Resistance to current flow along surface
Resistance to current flow through pore fluid
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 13: Controls on surface conduction
Key soil properties
Surface area
Mineral surface chemistry
10-1
1
10
102
10-2
10-1
10-2
10-3
10-4
10-5
σsurf (S/m)
Spor = surface area to pore volume ratio
Data are sandstones reported in Börner (1992)
Dashed line shows linear relationship between σsurf and Spor
Fine-grained particles, such as clay minerals, have a very large surface area so surface conduction increases with clay content

## Slide 14: Addition of pore fluid and surface conduction
Basic equation describing electrical conductivity in the presence of surface conduction
Log (σw)
Log (σsoil)
Pore fluid conductivity dominant
Surface conductivity dominant
σw
σsoil
intercept = σsurf
Linear plot
Logarithmic plot

## Slide 15: Measuring resistivity: rock cores
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 16: Measuring resistivity: soils
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 17: Laboratory measurements of resistivity of soils and rocks