## Slide 1: Tutorial: The “Magic” of Geophysical Inversion
Lee Slater
Department of Earth and Environmental Sciences, Rutgers University, Newark, NJ, USA

## Slide 2: Recap: apparent resistivity – just a measurement in units of resistivity
Apparent resistivity: the resistivity of a homogenous subsurface that the measured voltage and current are equivalent to
= geometric factor determined by the distances between the four electrodes (see Unit 3 for details)
is a complex function of the intrinsic resistivity of the subsurface depending on the sensitivity of the array – but it is not equal to any of the intrinsic resistivity values
Transfer resistance with units of ohms

## Slide 3: Apparent resistivity
Apparent resistivity: the resistivity of a homogenous subsurface that the measured transfer resistance is equivalent to
Per the definition, in this case of a single resistivity
A homogeneous subsurface

## Slide 4: Plotting 2D Electrical imaging datasets
V
I
A
B
N
M
n=1
n=2
n=3
n=4
a
na
a
We assign the raw apparent resistivity measurements to a location at the midpoint of the array and at a level (or pseudodepth) n determined by the electrode separation
In the dipole-dipole array the pseudo depth is the integer multiplier on the a spacing defining the distance between the current electrode pair and the voltage measurement electrode pair
Larger values of n mean deeper investigation depth – but with lower spatial resolution
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 5: Pseudo sections
Wenner (a = n ´ 5m)
50Wm
500Wm
100Wm
ra(Wm)
ra(Wm)
1
3
5
1
3
5
7
n
n
Resistivity model
Dipole-dipole (a=5m)
We can plot an apparent resistivity pseudo section but it won’t represent the true resistivity structure of the subsurface – this is where we need the magic of geophysical inversion
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 6
The process by which the transfer resistance or apparent resistivity measurements acquired from the surface are transformed into estimated images of the subsurface resistivity (or conductivity)
ra (Wm)
n=1
n=5
n=10
log10 (resistivity in Wm)
Forward
modeling
Inverse
modeling
Pseudo section
Resistivity distribution
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and applications to the near-surface Earth, In Press

## Slide 7
Hypothetical examples of electrical imaging of internal structure: (a) medical scan of an arm, (b) a tree trunk cross section, and (c) an internal survey of a dam. Modified from Gray (1918), Paulsen et al. (2006), Martin and Günther (2013), Busato et al. (2016)
Source: Falzone et al. (2020), Transport in Porous Media
The concepts of inversion are used in many fields and for many applications today. Geophysicists use these concepts to image into the Earth

## Slide 8: What do images mean?
Infer spatial variation in soil/rock type, chemistry of the fluids in the ground, water content……..
Increasing conductivity – increasing salinity of water in soils?; increasing water content?; increase in porosity; increase in fine-grained sediments?
Image of subsurface electrical conductivity from the Harrier Meadow survey
Notes: But what do these images really mean? Unit 2 covers the relationships between the electrical conductivity of soils and the physical and chemical properties of soils. Using Archie’s Laws, we learned that electrical conductivity increases with the salinity of the pore fluids, the porosity of the soil and the water content if the soil is not saturated. We also learned that fine grained materials such as clays also increase electrical conductivity. The changes in conductivity observed with electrical imaging result from changes in such factors. At Harrier Meadow we know that the soils are saturated beneath the top 20 cm so the changes in conductivity in this image most likely represent changes in salinity and/or changes in soil type. Distinguishing between such effects is best done using some direct sampling at a few locations – indeed, the interpretation of geophysical datasets is always improved with some direct observations. We will use some direct measurements to explore the significance of these conductivity images further in Unit 5.

## Slide 9: How does it work?
Synthetic pseudo section
Measured pseudo section (with errors)
Synthetic resistivity model
????
Forward modeling
Statistical comparison
`
UNKNOWN RESISTIVITY MODEL OF THE EARTH

## Slide 10: How does it work?
??
Forward modeling
ADEQUATE GOODNESS OF FIT?
NO
Revise synthetic resistivity model
Synthetic pseudo section
Measured pseudo section (with errors)
UNKNOWN RESISTIVITY MODEL OF THE EARTH

## Slide 11: How does it work?
Synthetic measurements
Field measurements (with errors)
??
Forward modeling
ADEQUATE GOODNESS OF FIT?
NO
Revise synthetic resistivity model
ITERATE
UNKNOWN RESISTIVITY MODEL OF THE EARTH

## Slide 12: How does it work?
FIELD SUBSURFACE RESISTIVITY ??
Forward modeling
ADEQUATE GOODNESS OF FIT?
YES
Synthetic pseudo section
Measured pseudo section (with errors)
ESTIMATED SUBSURFACE RESISTIVITY MODEL

## Slide 13: Forward modeling
i,j
i-1,j
i+1,j
i,j+1
i-1,j+1
i+1,j+1
i,j-1
i-1,j-1
i+1,j-1
z
x
Dx
Dz
Numerical approach to approximate a solution to a non-linear partial differential equation: finite difference or finite element discretization
Solve for distribution of voltages resulting from injection of current into a subsurface with varying resistivity

## Slide 14: How to assess goodness of ‘fit’?
Measured pseudo section (observed ra)
Synthetic pseudo section (synthetic ra)
measured ra
synthetic ra
Differences between modeled synthetic ra and measured ra should be small (and random)
relative ‘misfit’ (-)
1:1 line is perfect fit
relative frequency (-)

## Slide 15: How to revise the synthetic resistivity model?
PRIOR ITERATION
measured ra
synthetic ra
improve the goodness of fit
Make sure that model updates are consistent with geological expectation of subsurface structure
UPDATED MODEL
DATA CONSTRAINT
MODEL CONSTRAINT

## Slide 16: Selecting reasonable models
Making sure that model updates are consistent with geological expectation of subsurface structure
Changes to the model structure are done with a constraint that favors smooth (but likely to be geologically reasonable) models
True model
Model found by inversion
Source: Binley and Slater, 2020, Resistivity and induced polarization: theory and
applications to the near-surface Earth, In Press

## Slide 17: Balancing goodness of fit versus updating the model
High quality data (low measurement errors): improve the goodness of fit more by adding more structure to the inverted model
Low quality data (high measurement errors): accept a lower goodness of fit and a smoother (less structure model)
DATA CONSTRAINT
MODEL CONSTRAINT
weighted by the measurement errors

## Slide 18: The importance of measurement errors
CORRECT ERRORS -> optimal structure
ERRORS UNDERESTIMATED -> too much structure
ERRORS OVERESTIMATED -> not enough structure
The errors in the measurements need to be estimated. Incorrect errors will lead to (1) excessive image structure when errors are underestimated, or (2) excess smoothing of structure when errors are overestimated
Notes: Correct errors are a_wgt=0.001 and b_wgt = 0.005. Overestimated errors: a_wgt = 0.01 and b_wgt = 0.005. Underestimated errors: a_wgt = 0.0001 and b_wgt=0.005

## Slide 19: Reciprocal errors
V
I
A
B
N
M
Normal measurement
V
I
A
B
N
M
Reciprocal measurement
switched
A robust way to assess the errors in the measurements. The theory of reciprocity states that the normal and reciprocal measurement must have the same resistance (and hence apparent resistivity).
Differences between the two measurements quantify the errors

## Slide 20: Modification of model constraints
Anisotropic smoothing – stronger horizontal smoothing e.g. sedimentary layering
Isotropic smoothing
Anisotropic smoothing – stronger vertical smoothing e.g. mapping walls of a buried structure
Notes: Now let’s consider the model constraint. This can actually take many forms depending on the geophysicist’s expectation of the likely variations in model structure in the subsurface. By far the most commonly used model constraint is the smoothness constraint introduced in this unit. However, even this smoothness constraint can be adjusted to result in changes in the predicted inversion result. For example, the constraint can be set to favor stronger horizontal smoothing, or conversely to favor strong vertical smoothing. In this case, the changes to the model constraint result in subtle but important changes to the resolved model structure. We might use a horizontal constraint to image sedimentary layers deposited in a valley but we might use a vertical constraint to map walls of a buried structure.

## Slide 21: Addition of borehole electrodes
TRUE MODEL
SURFACE ELECTRODES ONLY
SURFACE ELECTRODES AND BOREHOLE ELECTRODES
borehole electrodes
Can result in dramatic improvement in image resolution at depth
But: expensive, invasive and sometimes impractical
PREDICTED INVERSION RESULTS

## Slide 22: Inversion: a pair of fuzzy glasses
S
Note: There is NO such thing as geophysical X-ray vision! No silver bullets!
G
Inversion of resistivity data is not like donning a pair of x-ray glasses
The fuzzy, indirect information obtained from electrical resistivity inversion should always be interpreted in conjunction with other available datasets.
Image courtesy of Fred Day-Lewis (USGS)