## Slide 1: Frequency-Ratio Method
Landslide Susceptibility Index (LSI)
Version: May 22, 2018
Notes: DO REMEMBER to include attribution information for all the figures you include. Even if you took the picture or made the diagram, it will make it easier later if we just have that recorded.
ALSO – it is much easier to make notes (at least preliminary ones) for each slide NOW compared to several months later. Think about the information that future instructors using this materials will need to know in order to understand what the point of the different slides are. If all the relevant text is on the slide, notes may not be necessary, BUT if there are images, most likely some notes will be needed for future users.

## Slide 2
DISCLAIMER: Studies using frequency-ratio methods as applied to landslides will often use different terminologies. In some studies, LSI refers to the sum of the frequency-for all factors. In other studies, LSI refers to each independent frequency-ratio number associated with each factor and the susceptibility (S) of landslides is the average of all LSI. In this module, we use the latter (refer to Chalkias et al., 2014 for additional details).

## Slide 3: Frequency-Ratio (FR)
FR methods are one of the most popular bivariate methods of analyzing landslide susceptibility (Korup and Stolle, 2014).
Very popular because:
  Friendly to end users (simple to use).
  Vulnerabilities to slope failure of individual factors can be investigated.
For the purposes of this module, FR values result in a Landslide Susceptibility Index (LSI).
Often, researchers will use the total area of a landslide to calculate the LSI, but it is also suitable to use point data referencing the headscarp of each landslide (initial point of failure).
  We will use headscarp data.
Notes: Korup O, Stolle A (2014) Landslide prediction from machine learning. Geol Today 30:26– 33. doi:10.1111/gto.12034

## Slide 4: The “math”
To calculate an LSI, a given factor (F) is categorized into n types (or subdivided into n classes).
The frequency ratio for each class (i) can be written as:
Notes: Modeled after Chalkias et al 2014.
Chalkias, C., Ferentinou, M., & Polykretis, C. (2014). GIS-Based Landslide Susceptibility Mapping on the Peloponnese Peninsula, Greece. Geosciences, 4(3), 176-190. doi:10.3390/geosciences4030176

## Slide 5: The “math” – con’t
Notes: Modeled after Chalkias et al 2014.
Chalkias, C., Ferentinou, M., & Polykretis, C. (2014). GIS-Based Landslide Susceptibility Mapping on the Peloponnese Peninsula, Greece. Geosciences, 4(3), 176-190. doi:10.3390/geosciences4030176

## Slide 6: The “math” – con’t
Notes: Modeled after Chalkias et al 2014.
Chalkias, C., Ferentinou, M., & Polykretis, C. (2014). GIS-Based Landslide Susceptibility Mapping on the Peloponnese Peninsula, Greece. Geosciences, 4(3), 176-190. doi:10.3390/geosciences4030176

## Slide 7: What do LSI numbers mean?
Positive LSI values indicate that the factor (Fi) favors the occurrence of landslides.
  The more positive, the greater this correlation.
Negative LSI values indicate that Fi does not favor the occurrence of landslides.
  The more negative, the worse the correlation.

## Slide 8: LSI Methods – an example from Arizona, USA
Classify factor.
-Can be classified based on:
-Natural Jenks
-Manual
-Equal Interval
-Etc…
Quantitative
Elevation (m) | Categories (Classes)
 | <569
 | 570-1056
 | 1057-1533
 | 1534-1976
 | >1976
Notes: INSTRUCTOR: this slide gives an example of how a quantitative factor, such as elevation, might be classified using ArcMap’s embedded classification method. A great way to get students to consider differences in methods is to draw a simple bell curve of data and draw equidistant lines (equal interval) to split the data. Using another color or line texture (dashed?) draw separating lines that are closely spaced together at the peak of the curve and more distant on either end (mimicking natural jenks). Have students consider what these classifications might mean. Equal interval means that the amount of data in each class varies heavily, with the most being in the center of the curve, while ‘natural jenks’ would have almost similar amounts of data. Draw other types of frequency curves (bimodal?) for further conversation/exploration.

## Slide 9: LSI Methods – an example from Arizona, USA
Classify factor.
Qualitative
-Much more subjective classification.
Aspect | Categories (Classes)
 | North
 | East
 | South
 | West
Notes: INSTRUCTOR: this is an example of how to classify something like Aspect. Have students think about the number of classes and their meaning. Is four classes enough? Do you need eight or six? In what way might the direction a slope is facing affect the processes that occur on these slopes? Guide students to consider solar radiation, rain/shadows, vegetation, etc…

## Slide 10: LSI Methods – an example from Arizona, USA
Classify factor.
Extract areas for each Fi.
Calculate LSI for each ith factor.
Elevation (m) | Categories (Classes) | LSI
 | <569 | -1.745
 | 570-1056 | 0.694
 | 1057-1533 | 0.142
 | 1534-1976 | 0.03
 | >1976 | -0.643
Notes: INSTRUCTOR: here the LSI is calculated for each factor using the final equation in slide six. You may opt to show students the automated code .txt file that is annotated to describe how the algorithm works.

## Slide 11: LSI Methods – an example from Arizona, USA
Classify factor.
Extract areas for each Fi.
Calculate LSI for each ith factor.
Analyze LSI data.
Factor | LSImin | LSImax | LSIrange | LSIst.dev.
Elevation | -1.745 | 0.694 | 2.439 | 0.935
Notes: INSTRUCTOR: Have students look at the LSI data in the table here. Is there a strong correlation? No correlation? What does the standard deviation tell you? (A large standard deviation with a very high/low LSI max/min suggests a single class factor plays a significant role, whereas a small st. dev. Suggests that the factor might night have too much of a role in landslide distribution). See slide 12 for additional example using Arizona elevation.

## Slide 12: LSI Analysis
Low-moderate categorization of elevation most favors landslides.
Extremely low and extremely high elevations do not favor landslides.
Elevation (m) | Categories (Classes) | LSI
 | <569 | -1.745
 | 570-1056 | 0.694
 | 1057-1533 | 0.142
 | 1534-1976 | 0.03
 | >1976 | -0.643
Factor | LSImin | LSImax | LSIrange | LSIst.dev.
Elevation | -1.745 | 0.694 | 2.439 | 0.935
Notes: Example of how this LSI data for elevation from Arizona might be interpreted. This also suggests that, since low-moderate categorization of elevation most favors landslides, the majority of landslides likely occur at the foothills of high topographic features leading into valleys.

## Slide 13: LSI Analysis
Refer to the document for the LSI analysis for the entire state of Arizona.
Discuss
  Why did the researchers choose these particular factors?
  Why did they choose the classifications that they did? Do you agree, or disagree with their classifications? What might you choose to do differently?
  What factors had the greatest impact? Does this make sense for Arizona? Why, or why not?

## Slide 14: Puerto Rico Vs. Arizona
What factors (see right side of slide) do you think will have the greatest LSI values (favor mass movements) in Puerto Rico? Why?
What about for Arizona? Why?
Elevation
Slope
Aspect
Mean Annual Precipitation (MAP)
Lithology
Landcover
Notes: To the teacher: Write the predictions down, or list them on the board!

## Slide 15: The Datasets
Arizona (Area: )
Az_Elevation
Az_Slope
Az_Aspect
Az_Maprecip
Az_Lithology
Az_Landcover
AzLandslides75
AzLandslides25
TOTAL LANDSLIDES: 620
Puerto Rico (Area: )
PR_Elevation
PR_Slope
PR_Aspect
PR_Maprecip
PR_Lithology
PR_Landcover
PRLandslides75
PRLandslides25
TOTAL LANDSLIDES: 2,053*
Notes: Teachers: Ask what the difference in landslide numbers versus area might mean!
*There are actually 41,053, but for performance reasons only a small subset is used!