## Slide 1: Introduction to Lidar

## Slide 2: Lidar
The next several slides (in blue) adapted from a presentation by Edwin Nissen done in collaboration with Ramon Arrowsmith, Srikanth Saripalli, and Aravindhan Krishnan. Additional modifications by Bruce Douglas and Beth Pratt-Sitaula
Notes: General comments about the evolution of ways in which we display topographic information in a 2-D fashion

## Slide 3: Topography in the Modern Era
Topographic mapping is now an automated, remote sensing process, using the distortions obtained in satellite or air photos with oblique viewing angles.
A digital elevation model (DEM) is the modern equivalent of a topographic map, with elevation information gridded into pixels.
By shading the topography artificially (“hillshading”), you can identify more details than are visible from the heights alone.
Airborne and terrestrial lidar systems produce a significantly higher density of measurements and can permit the removal of vegetation from the DEM.
Notes: General comments about the evolution of ways in which we display topographic information in a 2-D fashion

## Slide 4: Digital elevation models
“A DEM is a digital data set, a grid of numbers representing the elevation of the surface, sampled at a regular spacing, and with known coordinates.”
How are DEMs created?
From older (triangulation/clinometry) and newer optical photo-based methods of topographic data sets used to construction topographic maps
DEMs from optical satellite images
Lidar
Notes: Definition of the acronym DEM with various means of creating these types of products. Since this presentation focuses on LiDAR, details of the latter are given in subsequent slides.

## Slide 5
Altitude
600 – 1000 m AGL
Swath width
up to 1500 m
Wavelength
500 – 1000 nm
Pulse rate
10s – 100s kHz
Footprint
15 – 20 cm
Accuracy
5 – 15 cm vertical
20 – 30 cm horizontal
GPS
IMU
GPS base station
Introduction to Airborne lidar topography
Notes: Initial figure in a set of schematic diagrams that show component of airborne lidar collection starting with data collection procedure. Basic parameter details given along with linking of onboard navigation and location coupled with ground-based information.
Image source for remaining slides: Unless otherwise noted, remaining images are reused with permission from presentation by Edwin Nissen (Colorado School of Mines) done in collaboration with Ramon Arrowsmith, Srikanth Saripalli, and Aravindhan Krishnan.

## Slide 6
“Point cloud” collection of irregularly spaced x, y, z spot heights
early lidar data sets had ~1 point per sq. m
modern data sets have >10 points per sq. m
1 m
1 m
Notes: Initial data set shown relative to a fixed grid cell of a specified size

## Slide 7
“Point cloud” collection of irregularly spaced x, y, z spot heights
early lidar data sets had ~1 point per sq. m
modern data sets have >10 points per sq. m
Digital Elevation binning algorithm converts point cloud into regular grid
define node spacing and search radius
choose mean, distance weighted mean, maximum or minimum
Model (DEM)
Notes: Point cloud to regularly spaced grid and means of incorporating appropriate data into single grid point

## Slide 8
“Point cloud” collection of irregularly spaced x, y, z spot heights
early lidar data sets had ~1 point per sq. m
modern data sets have >10 points per sq. m
Digital Elevation binning algorithm converts point cloud into regular grid
define node spacing and search radius
choose mean, distance weighted mean, maximum or minimum
Model (DEM)
Notes: Final gridded data set with light-dark scale used to indicate elevation information for each cell

## Slide 9
Shuttle Radar Topography Mission (SRTM)
released in 2005
90 m pixel size
coverage of latitudes <60o
ASTER Global Digital Elevation Model (GDEM)
released in 2009
30 m pixel size
Coverage of latitudes <83o
Airborne Light Detection and Ranging (LiDAR)
also known as
Airborne Laser Swath Mapping
(ALSM)
1 km
Notes: Comparison of varying scales of resolution for different platforms/resource types used to generate DEMs

## Slide 10
Canopy
Canopy
Ground
Waveform
Discrete returns
Lidar and vegetation
Notes: Schematic sequence showing initial and subsequent returns from reflectors. For vegetated areas, the first several returns may be from vegetation with the last return coming from the land surface.

## Slide 11
Lidar and vegetation
Digital Elevation binning algorithm converts point cloud into regular grid
define node spacing and search radius
choose mean, distance weighted mean, maximum or minimum
“vegetation off”
or “bare earth”
Digital Elevation binning algorithm converts point cloud into regular grid
define node spacing and search radius
choose mean, distance weighted mean
“vegetation on”
Denali earthquake (Mw 7.9)
Alaska, 3rd Nov 2002
Notes: Example of vegetation on and off

## Slide 12: “Seeing” through vegetation to find landslides
Notes: Vegetation makes it hard to see the landslide in the air photo (left). A bare earth lidar image the same area shows clear evidence of the landslide area and scarp. Red dashed line highlights to scarp.
Image from Oregon’s DOGAMI (Department of Geology and Mineral Industries) – Public Domain
https://www.oregongeology.org/pubs/Publications_Center_Permissions_and_Credits.pdf

## Slide 13: North Fork Stillaguamish Valley, WA
The "Oso" landslide: 3/22/14

## Slide 14
North Fork Stillaguamish River 2014 – Google Earth
Google Earth

## Slide 15
Same Region– Bare Earth Lidar image
(pre Oso 2014 landslide)

## Slide 16
Steelhead Haven
2014 landslide
Originated here,
Running out over
The Steelhead
Haven comunity

## Slide 17
Notes: OpenTopography provides one of the largest openly available lidar data portals.
(http://www.opentopography.org/)

## Slide 18
Notes: Interactive map that shows location of available data

## Slide 19
Notes: Example of various trade-offs when using airborne lidar data

## Slide 21
Terrestrial Laser Scanning (TLS)
Lidar units are now available as a tripod-mounted system.
Typically these systems have a range of 500–2000 m.
These can be used to scan outcrops, buildings, fault scarps, volcanoes, landslides, glaciers, beaches . . .
Notes: Left-hand top and bottom images: show students collecting terrestrial lidar data of a normal fault and an example of the analysis of fault displacement.
Right hand image: A string of multiple terrestrial lidar scans to create a 1-km scale point cloud data set for the purposes of geological mapping and structural interpretation.
Image sources: Nathan Niemi (U of Michigan) and Bruce Douglas (Indiana University)