## Slide 1
NAS 338
Water Quality
Prof. Hill
The Wicked Problem of Nutrient Pollution
Mississippi River, Wabasha, MN
Image: Aaron Lavinsky, Star Tribune
Notes: https://www.startribune.com/eye-in-the-sky-watches-the-mississippi-for-nasa/391342591/

## Slide 2
Problems difficult to formulate and impossible to “solve” because of incomplete, confusing, or contradictory information and involving innumerable stakeholders with conflicting perceptions, needs, and values (Churchman, 1967)
Wicked problems exist in a world of interconnected natural and human systems, including commerce, which drives economies
Wicked Problems
Notes: Source: https://its.ucr.edu

## Slide 3
Current SDGs were adopted by the UN in 2015
Set of interconnected goals to tackle environmental, political, and social challenges facing our world
Used to frame 2030 UN targets (e.g. European Union)
https://sdgs.un.org/goals
Notes: Source: https://its.ucr.edu

## Slide 4
Nitrogen and SDG Goal: Example
Notes: Source: https://its.ucr.edu

## Slide 5
Notes: https://www.usgs.gov/special-topics/water-science-school/science/water-cycle-diagrams

## Slide 6
This is a watershed…
Headwaters
Mouth
Conceptually useful for water budget studies
Area of land where all the water that is under it or drains off it goes into the same place
John Wesley Powell:
  "that area of land, a bounded hydrologic system, within which all living things are inextricably linked by their common water course and where, as humans settled, simple logic demanded that they become part of a community"
Watersheds come in all shapes and sizes, crossing county, state, and national boundaries. No matter where you are, you're in a watershed!
Notes: Fall Creek Watershed, Hill, N. B.
Wesley Swingley

## Slide 7
US Basins: Mississippi River Drainage Basin
Gulf of Mexico
Notes: Grasshopper Geography Etsy shop

## Slide 8
Trophic Status
https://www.rmbel.info/primer/lake-trophic-states-2/

## Slide 9
Eutrophication
Perez-Ruzafa et al., 2018

## Slide 10
https://www.fieldmuseum.org/blog/climate-change-and-lakes-look-pea-soup
Eutrophication
N (nitrogen) and P (phosphorus) loaded into water bodies as both diffuse- and point-source pollutants
  Diffuse: fertilizer runoff and erosion, landfill runoff and erosion, manure runoff and erosion
  Direct: wastewater treatment plant effluent, industrial effluent
N, P, K (potassium) are vital macronutrients for plants, algae, and cyanobacteria; P is often a limiting nutrient so when other nutrients are available in excess and P is added it will destabilize the aquatic ecosystem; other limiting nutrients, such as S (sulfur) may do the same
Additionally, atmospheric diffusion is reduced and baseline respiration increases (until oxygen becomes limited)
Decomposition will continue after oxygen is depleted but it will be anaerobic rather than aerobic decomposition
  Anaerobic is less efficient and releases greenhouse gases (methane and nitrous oxide) that are more potent than carbon dioxide along with sulfide (an air pollutant)

## Slide 11
Eutrophication (Anthropogenic)

## Slide 12
Eutrophication (Ocean)

## Slide 13
Harmful Algal Blooms (HABs): Red Tide
Red Tide, Florida
https://oceanservice.noaa.gov/facts/redtide.html
Notes: Show video
What can *you* do about it?
Here are some ways that you can make a difference in preventing eutrophication:
Reduce fertilizer use. Over-fertilizing your land can lead to runoff of nutrients into local water bodies.
Purchase phosphorus-free laundry detergents.
Reduce water usage during rain storms (laundry, dishwashing, etc.). When there is excess water in sewage systems, excess wastewater is dumped into lakes. Learn more about how this is happening in Chicago and how to get involved.
Reduce your carbon footprint. You can reduce carbon emissions and mitigate climate change in many ways, such as recycling and composting, riding a bike or walking, unplugging chargers and appliances when not in use, buying local produce, and more.

## Slide 14
Alosairi et al., 2021, Ecotoxicology and Environmental Safety

## Slide 15
Alosairi et al., 2021, Ecotoxicology and Environmental Safety

## Slide 16
Gulf of Mexico Dead Zone
NOAA
Nutrient loading
Notes: https://wusfnews.wusf.usf.edu/environment/2021-08-04/gulf-dead-zone-is-larger-than-average

## Slide 17
Eutrophication (Factors & Effects)
Ferreira et al., 2011

## Slide 18
Water Quality Indicators
Variable | Oligotrophic | Mesotrophic | Eutrophic
Total Nitrogen (mg/L) | <0.5 | 0.5-1.5 | >1.5
Total Phosphorus (mg/L) | <0.025 | 0.025-0.075 | >0.075
Chlorophyll a (mg/L) | <2 | 2-15 | >15
Primary productivity (g m-2 d-1) | <0.25 | 0.25-1.0 | 1.0
Secchi disk visibility (m) | >8 | 2-8 | <2
Boyd, 2020

## Slide 19
Biochemical Oxygen Demand
Streams with low dissolved oxygen (DO) may be considered polluted
BOD: amount of oxygen required for biochemical decomposition processes
Image: fondriest.com
Notes: Hill, N. B.

## Slide 20
Biochemical Oxygen Demand
Streams with low dissolved oxygen (DO) may be considered polluted
BOD: amount of oxygen required for biochemical decomposition processes

## Slide 21
Biochemical Oxygen Demand
Streams with low dissolved oxygen (DO) may be considered polluted
BOD: amount of oxygen required for biochemical decomposition processes
Notes: Hill, N. B.

## Slide 22
Some Point & Nonpoint Sources
Notes: Boyd, Water Quality, 2020

## Slide 23
Nitrogen Cycle
Nitrogen gas
(N2) in air
Nitrogen
oxides in air
N-fixing
by lightning
Industrial
N-fixation
Fossil fuel
combustion
Denitrification
N-compounds
Fertilizer
Non-N-fixing
producers
Nitrogen-
fixing producers
Legumes
Cyanobacteria
Non-legume
crops
Manure
compost
Animals
Soil bacteria
Nitrate
compounds
NO3-
Consumers
Soil bacteria
Ammonium
compounds
NH4+
© 2017 Pearson Education, Inc.

## Slide 24
Nitrogen Fixation
Atmospheric fixation by lightning
Biological fixation
Industrial fixation (Haber-Bosch process)
  At high P (15-25 MPa) and T (300-500°C), N2 reacts with 3H2 (from natural gas or petroleum) driven by a catalyst (K2O, CaO, SiO2, or Al2O3) to form 2NH3 (used directly or oxidized to NO3-)
Notes: Hill, N. B.

## Slide 25
Energy Use in N-Fertilizer Production
Nitric acid (HNO3)  nitrate (NO3-)
  Birkeland-Eyde process
  Electrical arcs react atmospheric N2 with O2
Calcium cyanamide (Ca(CN)2)  ammonia (NH3)
  a.k.a. Nitrolime
Ammonia (NH3)
  Haber – Bosch process (high temp & pressure); coke formed from heating coal or oil in the absence of air
  Electrolysis from water (H reacted with N)
  Electrolysis from methane (H reacted with N)
Partial oxidation
  Oxidation of ammonia to nitrate
Steam reforming
  Ammonia produced from steam methane
Woods et al., 2010; Behrens et al., 2020

## Slide 26
Plant Uptake
Plants can absorb combined nitrogen from water in the form of ammonia (NH3), ammonium (NH4+), nitrite (NO2-), and nitrate (NO3-)
Ammonium and nitrate preferred
Nitrate reductase:
Amino acids synthesis:
Phytoplankton contain 5-10% of their dry weights as protein nitrogen
Notes: Hill, N. B.

## Slide 27
Mineralization & Immobilization
Some chemicals cycle quickly and are readily regenerated for biological activity
  Typically have a gas phase, are soluble, and carried by hydrologic cycle (e.g., O and N)
Other chemical elements are relatively immobile and returned by geological processes
  Typically lack a gas phase and are insoluble (e.g., P)

## Slide 28
Nitrogen Cycle

## Slide 29
Environmental Impacts
Ammonia diffusion
  Greatest at high pH (>8)
  Reacts with sulfuric and nitric acids to form fine particulates
Ammonia toxicity
  Major excretory product of aquatic animals
  Toxic if it cannot be excreted (when aquatic concentrations are too high)
  Elevated blood pH, disruption of enzyme systems and membrane stability, increased water uptake, increased oxygen consumption, gill damage, histological lesions
Nitrite toxicity
  Occurs in waters with low oxygen
  Greater concern in freshwater than saltwater
  Absorbed by fish and other organisms
  Nitrite reacts with hemoglobin (in fish blood) to form methemoglobin, leading to functional anemia (brown blood disease)
  Lowers the ability of crustacean blood to transport oxygen

## Slide 30
Environmental Impacts
Gas bubble trauma
  Gases dissolve in the blood of aquatic organisms
  Water becomes supersaturated with air due to cooling water, air leaks in pumps, water entraining air when it falls over dams, etc.
Air pollution
  Combustion of fossil fuels produce nitrogen oxides (NOx) which are hydrolizd to nitric acid in the atmosphere
  Contribute to acid rain
Greenhouse gas emissions
  Incomplete denitrification
  Nitrous oxide (N2O) is a greenhouse gas with warming potential ~300 times greater than CO2

## Slide 31
Where is Phosphorus?
In living organisms
  Nucleic acids (DNA & RNA)
  Cellular energy storage, transfer, and use (ADP & ATP)
  Lipids
  Plant tissues (phytic acid)
    Digestible by ruminant animals thanks to the enzyme phytase
In minerals
  Phosphate group
    Apatite is the most common Ca5(PO4)3(F, Cl, OH)
    Turquoise CuAl6(PO4)4(OH)8•5H2O
In industrial and at home
  Fertilizers and pesticides
  Cleaning agent and water softener (trisodiumphosphate)
  Beverages (phosphoric acid in cola)
  Flavor intensifier and emulsifier in food
  Matches and fire retardants
  Surfactants and lubricants

## Slide 32
Peruvian Pelicans
Macabi
Image: Ernesto Benavides
https://www.audubon.org/news/holy-crap-trip-worlds-largest-guano-producing-islands
Notes: Give students a few minutes to read this

## Slide 33
Liebig’s Law of the Minimum
Phosphorus is often the limiting nutrient for phytoplankton productivity
Notes: Boyd, Water Quality, 2020

## Slide 34
Organic Fertilizers: animal manure, crop residues, fresh vegetation (green manure), compost
Inorganic Fertilizers (mined/synthetic) more susceptible to leaching and runoff
Gilbert, 2020, Biogeochemistry
Fertilizer Use (tonnes/yr.)
Fertilizer Application

## Slide 36
Terrestrial Phosphorus Cycle
W
Notes: Fink et al., 2016

## Slide 37
Aquatic Phosphorus Cycle
Notes: Boyd, Water Quality, 2020

## Slide 38
What are Water Quality Standards?
U.S. EPA
Foundation of the water quality-based control program mandated by the Clean Water Act (18 Oct. 1972)
Clean Water Act
  Sec. 101. Declaration of Goals and Policy
    The objective of this Act is to restore and maintain the chemical, physical, and biological integrity of the Nation’s waters…
    …
    it is the national goal that wherever attainable, an interim goal of water quality which provides for the protection and propagation of fish, shellfish, and wildlife and provides for recreation in and on the water achieved by July, 1983…

## Slide 39
Laws, Regulations, Guidance
U.S. EPA
Laws
  Passed by Congress, signed by the President
  Impose requirements (i.e. “must”)
  Published in the United States Code (U.S.C.)
Regulations
  Substantive rules that supplement a statute
  Have the force and effect of law (“must”)
  Authority comes from the law
  Involve “notice and comment” rulemaking
Guidance/Policy
  Does not have force of law (only “should”)
  Notice and comment not required
  Not binding on Agency or public

## Slide 40
Law: Clean Water Act
U.S. EPA
Objective: “restore and maintain the chemical, physical, and biological integrity of the Nation’s waters…” (Clean Water Act 101 (a))
Interim goal: “water quality which provides for the protection and propagation of fish, shellfish, and wildlife and provides for recreation in and on the water…” wherever attainable by 1983 (Clean Water Act 101 (a)(2))
Implementations: States, Territories, and authorized Tribes
Relevant Sections: 101 (Goals and Policy), 301 (Technology Based Effluent), 302 (Water Quality Based Effluent), 303 (WQ Standards and Implementation), 319 (Non-point Source Management), 401 (State/ Tribal Certification), 402 (Point Source Permitting, NPDES), 502 (Definitions: Navigable, Pollutant…), 510 (State/ Tribal Authority), 518 Indian Tribes

## Slide 41
Water Quality Standards
U.S. EPA
303(c): Law
Define the water quality goals for a waterbody
Provide a regulatory basis for many actions
  Reporting on water quality conditions and status
  Developing water quality based effluent limits in National Pollutant Discharge Elimination System (NPDES) permits for point sources
  Setting targets for Total Maximum Daily Loads (TMDLs)
40 CFR 131: Regulations
Designated Uses (131.10)
Criteria (131.11)
Antidegradation (131.12)
Domain: Traditional navigable waters (TNW); interstate waters; non-navigable tributaries that are either relatively permanent or have significant nexus to TNW; Non-tributary wetlands, adjacent to TNW, abut relatively permanent water, nexus to TNW

## Slide 42
Point Source Pollution
U.S. EPA
Point source: “Any discernable confined, discrete conveyance including… any pipe, ditch, channel… [etc.] from which pollutants are or may be discharged. This term does not include agricultural storm water discharges and return flows from irrigated agriculture.” (Section 502(14), Clean Water Act)
Examples of activities:
  National Pollutant Discharge Elimination System (NPDES) permits (Sec. 402)
  Section 404 permits for discharge of dredged or fill material
  Activities subject to Section 401 (federal permits/ licenses)

## Slide 43
Non-point Source Pollution
U.S. EPA
Non-point source: “Any source of water pollution that does not meet the legal definition of ‘point source’.”
Can be thought of as polluted runoff, which cannot be tied to a single source
In general, WQ Standards not directly implemented through NPS activities
NPS Management Program (Section 319): voluntary program to reduce NPS pollution

## Slide 44
WQ Standards Schematic
U.S. EPA

## Slide 45
WQ Standards Schematic
U.S. EPA

## Slide 46
What are designated Uses?
U.S. EPA
Designated uses are “those uses specified in State or Tribal Water Quality Standards regulations for each water body or segment whether or not they are being attained.”
May be thought of as:
  Water quality goals
  Management objectives
  Communication tools
  Functions and/ or activities that are supported by a level of water quality
Examples:
  Protection and propagation of fish, shellfish, and wildlife
  Recreation in and on the water
  Public water supply
  Agriculture
  Navigation

## Slide 47
Designated Uses: Example
U.S. EPA
Pyramid Lake Paiute Tribe
  Calls designated uses “Beneficial Uses”
  20 different Beneficial Uses”
    Cold freshwater aquatic habitat
    Water contact recreation
    Primary contact ceremonial use
    Extraordinary aesthetic value
    Others
Designated Uses are the activity + the water quality to support that activity
35 miles NE of Reno, NV

## Slide 48
WQ Standards Schematic
U.S. EPA

## Slide 49
Water Quality Criteria
U.S. EPA
A numeric value (e.g. magnitude, duration, and frequency) or narrative statement
  Example numeric: “To protect Aquatic Life, Dissolved Zinc shall not exceed 90 micrograms per liter as a one hour average more than once every three years.”
  Example narrative: “To protect all Designated Uses, there shall be no toxic materials in toxic amounts.”
Represent a level of water quality that supports a particular use
EPA Publishes Water Quality Criteria recommendations under Section 304(a) of the Clean Water Act (a.k.a. “EPA’s 304(a) criteria recommendations”)

## Slide 50
Water Quality Criteria Requirements
U.S. EPA
40 CFR 131.11
  States/ Tribes should adopt numeric Criteria based on:
    EPA’s 304(a) Criteria recommendations
    304(a) recommendations modified to reflect site specific conditions
    Other scientifically defensible methods
  States/ Tribes should adopt narrative Criteria:
    Where numeric Criteria cannot be established
    Or to supplement numeric Criteria
Types of Criteria:
  Aquatic life, human health, bacterial, biological, nutrient, other (e.g. sediment)

## Slide 51
Numeric Criteria: Example
U.S. EPA

## Slide 52
National Primary Drinking Water Regulations
Contaminant | MCLG (mg/L) | MCL (mg/L) | Potential Health Effects from Long-Term Exposure Above the MCL (unless specified as short-term) | Sources of Contaminant in Drinking Water
Nitrate, NO3- (measured as Nitrogen) | 10 | 10 | Infants below the age of six months who drink water containing nitrite in excess of the MCL could become seriously ill and, if untreated, may die. Symptoms include shortness of breath and blue-baby syndrome. | Runoff from fertilizer use; leaking from septic tanks, sewage; erosion of natural deposits
Nitrite, NO2- (measured as Nitrogen) | 1 | 1 |  | 
Nitrate contamination of groundwater is a problem particularly in rural areas. Agricultural activity contributes fertilizers and animal wastes to water sources.
  Soluble and difficult to remove from water supplies.
  Infants around one year old and younger can metabolize nitrate to nitrite. Nitrite ions then form complexes with heme, and the baby can turn blue and die, methemoglobinemia (blue baby syndrome).
Notes: MCLG: Maximum contaminant level goal
U.S. EPA

## Slide 53
From USGS Circular 1225, The Quality of Our Nation's Waters.
Notes: Wesley Swingley

## Slide 54
Notes: Wesley Swingley

## Slide 55
Alexander et al., 2008, Environmental Science and Technology

## Slide 56
Nitrogen loading to the Mississippi River Basin by decade by source. Sources include human waste, atmospheric deposition, fertilizer, Biological Nitrogen Fixation (BNF), Manure, pre-Settlement landscape sources (Van Meter et al., 2016).
Notes: Wesley Swingley

## Slide 57
Tool used by businesses to map out key stakeholders (individuals and groups) and their relationship to and influence on the company.
Visual representation of the entire system, the parts and how they are all connected.
Identify the components, including stakeholders, involved in Nitrogen in the Water System and map the relationships among them.
Stakeholder Mapping

## Slide 58
Examples of Concept Maps
(Mind Mapping)
Notes: Source 1: https://www.conceptdraw.com/How-To-Guide/concept-map
Source 2: https://www.pinterest.co.uk/pin/537476536748491475/

## Slide 59
Either by hand or using PowerPoint, Canva, Mural (or other online mapping program), you and your teammates will create a unified map of the stakeholders involved.
Add system components. Write the primary topic at the center of your map: “Nutrient Pollution in the Mississippi River.” Add items representing key components of the complex system. Keep each item simple (aim for 1-3 words per item, e.g., “Drinking Water,” “Plastics Manufacturers,” “City Council”). Include a rough hand-drawn sketch (e.g., an icon, cartoon, stick figure) to represent each major item. Use materials posted to BB to help you brainstorm.
Indicate relationships among the components. Draw arrows and label them with linking words to indicate relationships among items (e.g., “A —controls—> B,” “A —contaminates—> B,” “A —supports—> B”). Use colored pencil, symbols, or thin/thick lines to underscore especially strong or important relationships among items (e.g., use thicker lines for stronger relationships). You may need to rearrange some items during this step.
Upload your map to Blackboard. If you created your map using light handwriting in pencil, reinforce key elements using a pen (black or blue) or a marker (e.g., black sharpie) to ensure that your map is high contrast enough to be visible from a distance. Then, scan or take a picture of your completed concept map.
Create a Stakeholder Map

## Slide 60
What did you identify as the key components?
What are some important relationships that you identified?
Who are some of the key stakeholders? (individuals or groups with an interest in or impacted by the issue)
Discussion

## Slide 61
Wicked Problem Groups
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
Stakeholder Mapping & Town Hall Meeting