## Slide 1
Version: Feb 6, 2019
Using SAR to Measure Ice Velocity
Notes: Image of the velocity of the ice sheet over West Antarctic as determined using SAR data. The color bar indicating the values associated with the colors. https://svs.gsfc.nasa.gov/4168

## Slide 2: SAR (Synthetic Aperture Radar) satellite data
…is used to determine ice velocities using repeat imagery in two ways
InSAR
Speckle tracking (similar to feature tracking, which is done with optical images)

## Slide 3: InSAR
Interferometric
Synthetic Aperture
Radar
pretend you have a big radar antenna
use wave interference
emit microwaves, measure echoes
Notes: SAR (Synthetic Aperture Radar) is an imaging technique in its own right that uses the amplitude (intensity) of backscattered radar from the ground as a means of imaging it. A single image acquisition is all that is needed to produce a SAR image. Typically we do not use the phase of a single SAR image for imaging purposes.
On the other hand, we can use the phases of multiple SAR images. InSAR is a method that uses two or more SAR images to measure movements of Earth’s surface, by calculating the interference between the phases of the SAR images.
Elements of this InSAR presentation are taken from a presentation developed by Gareth Funning (UC Riverside) for GETSI module “Imaging Active Tectonics” Unit 3. https://serc.carleton.edu/details/files/63910.html

## Slide 4: SAR: how it works
Satellite emits radar pulse
Radar is backscattered
Amplitude (intensity) and phase of echo is recorded at the satellite
Glacier flow
Notes: The radar antenna on a satellite (shown here is ERS-1, the first long-lived orbiting SAR satellite, launched in 1991) is both an emitter of radar and a detector of radar. A pulse of microwave radiation is emitted toward the ground, and some of it is scattered back to the satellite. The antenna records both the amplitude (intensity) and phase of the backscattered radar. A typical radar satellite makes over a thousand such measurements every second (in the case of ERS-1, 1680 measurements per second).
Image from: https://nsidc.org/sites/nsidc.org/files/technical-references/GIMP-ATBD-Version2.pdf
Landsat image of the Kangerdlussuaq Glacier is used for illustration purposes.

## Slide 5
Phase ==> records distance between satellites and earth.
Amplitude==>records terrain slope and surface roughness.
Phase change implies ground motion such as glacier/ice movement, landslide, faulting …
Time-series approach=> two or more images of the same area taken at different times.
InSAR images record:
If distance between sensor and repeat target is non-zero following corrections==> motion
Notes: SAR imaging uses amplitude (intensity) of backscattered echoes. Radar sees through clouds—all-weather imaging is possible.
Don’t need illumination by the Sun—can image day and night
Surface roughness and slopes control the strength of the backscatter

## Slide 6: Phase
Phase is a function of the distance from the satellite to the ground.
~780 km
~6 cm
ERS-1
Glacier flow
Notes: In this example, the ERS-1 satellite has a wavelength of ~6cm (called “C-band”), so the resolution of changes is ½ the wavelength and thus ~3cm.
Recall that one wavelength of path length is equivalent to 2π of phase. Given that radar satellites orbit at several hundred km of elevation, it is not feasible to count the number of phase cycles for a single image . . .
Image from: https://nsidc.org/sites/nsidc.org/files/technical-references/GIMP-ATBD-Version2.pdf
Landsat image of the Kangerdlussuaq Glacier for illustration purposes.

## Slide 7: InSAR: How it works
Pass 1
Pass 2
Glacier flow
Notes: . . . So what we do is compare (difference) the phase from two different passes of the same satellite over the same point on the ground. Assuming that we can correct for the position of the satellite (and we can), then any difference in phase between the two passes must be related to a change in distance between the satellite and the ground (i.e. a movement of the ground or the ice or glacier in this case).
In the example shown here, there is no change between the two passes (actually they are the same image), so we would determine no movement.

## Slide 8: InSAR: How it works
Pass 1
Pass 2
April 5, 2001
April 14, 2001
Phase=2
Phase shift due to ice movement.
Phase=1
Glacier flow
Notes: In this case there is change (although to the human eye, it would be hard to detect) between the two passes taken 9 days apart, so we can detect a phase shift when we subtract the phase of the second image from the phase of the first!
It is important to note that we can only measure displacement of the ground toward or away from the satellite, in the line-of-sight direction between the two. Everything we measure is a “line-of-sight” displacement.
For InSAR-derived velocities, researchers typically use the most frequent repeat times available – especially for fast-moving areas where flow is over a kilometer per year. Sentinel-1 satellites have repeat times of 6 days. Other satellites range may only repeat every ~30–90 days

## Slide 9: InSAR: How it works—Summary
Phase shift varies in different parts of the ice because of different velocities
One interferogram records motion in only one direction (Line of Sight), orthogonal to the flight path.
Assuming surface-parallel ice movement, interferograms from ascending and descending orbits can be combined to create 3D motion.
However, surface-parallel ice flow assumption does not work well unless the slopes are low and both accumulation and ablation are modest.
If no separate orbit SAR data, the ice-flow direction can be estimated from the direction of maximum averaged over an area larger than the thickness of the ice.
Notes: It is important to note that the only way we know that there has been movement is if different areas of the ice/glacier move with different amounts—InSAR makes measurements of relative deformation. If the whole area moved by the same amount we would not see any relative phase shift. In the Landsat image shown here we would expect the glacier/ground would move farther away from the satellite.

## Slide 10: Speckle tracking
Computer algorithm scans the intensity SAR for identifiable patterns in the pixels (“speckles”) and measure how much they shift between scenes.
Can help to think of “feature tracking” with optical satellite data wherein identifiable features are tracked over time.
Initial image
Glacier
Second image

## Slide 11: Speckle tracking
Speckle tracking calculates probabilities that a patch of “speckles” is the same patch of ice but moved.
Pairs of SAR images are co-registered with sub-pixel accuracy.
Co-registration is from cross-correlation of speckle patterns.
These registration offsets provide a vector estimate of displacement, although with poorer resolution and accuracy than conventional interferometry.
Initial image
Second image
Glacier
Example of how resulting vector field looks
Notes: Image from: https://nsidc.org/sites/nsidc.org/files/technical-references/GIMP-ATBD-Version2.pdf
Some of the text by Ian Joughin (UW). Used with permission

## Slide 12: Velocity Images of Antarctica and Greenland
High spatial variability is very challenging to fully capture
Final products are error-weighted mosaics of 100s–1000s of interferograms and speckle tracking vector fields
Notes: These maps demonstrate that ice sheet ice velocity is highly variable, and that there are certain regions of the ice sheets referred to as ice streams that transfer ice from the interior of the ice sheets to the ocean. The combination of InSAR and speckle tracking methods are needed in order to capture the large spatial variability.
https://nsidc.org/sites/nsidc.org/files/images/data/measures/0484v2/SampleImage.png (public domain)
https://nsidc.org/data/nsidc-0484
References for above Images and related videos
http://nsidc.org/data/NSIDC-0670#
http://nsidc.org/data/measures
https://www.youtube.com/watch?v=GDXq8Oa5d5Q
https://www.jpl.nasa.gov/video/details.php?id=1015
Further information on ice streams is available at: http://www.antarcticglaciers.org/modern-glaciers/types-of-glacier-2/ice-streams/

## Slide 13: Animation: Antarctica on the Move
Notes: Antarctica on the Move
“While Antarctica may appear stationary, it is actually a mosaic of moving ice sheets. Ice is naturally transported from the interior regions (where it accumulates from snowfall) to the coastal regions and is discharged to the ocean as tabular icebergs and ice-shelf melt water. This visualization shows the velocity of ice on Antarctica representing hundreds to thousands of years of motion. Ice velocity is color coded on a logarithmic scale with values varying from 1 meter per year (brown to green) to 3000 meters per year (green to blue to red). These observations have vast implications for our understanding of the flow of ice sheets and how they might respond to climate change in the future and contribute to changes in global sea level. “
SVS Animation 3848 - NASA Research Leads to First Complete Map of Antarctic Ice Flow

## Slide 14: Additional References
Joughin, I. (2002). Ice-Sheet Velocity Mapping: A Combined Interferometric and Speckle-Tracking Approach. Annals of Glaciology, 34, 195–201.
Joughin, I., Smith, B., Howat, I., Scambos, T. Greenland Ice Mapping Project 2 (GIMP-2) Algorithm Theoretical Basis Document Version 2, A NASA MEASURES PROJECT. https://nsidc.org/sites/nsidc.org/files/technical-references/GIMP-ATBD-Version2.pdf
König, M., Winther, J. G., & Isaksson, E. (2001). Measuring Snow and Glacier Ice Properties from Satellite. Reviews of Geophysics, 39(1), 1–27.
Mohr, J. J., Reeh, N., & Madsen, S. N. (1998). Three-Dimensional Glacial Flow and Surface Elevation Measured with Radar Interferometry. Nature, 391(6664), 273.
Palmer, S., Shepherd, A., Björnsson, H., & Pálsson, F. (2009). Ice Velocity Measurements of Langjökull, Iceland, from Interferometric Synthetic Aperture Radar (InSAR). Journal of Glaciology, 55(193), 834–838.
Rott, H. (2009). Advances in Interferometric Synthetic Aperture Radar (InSAR) in Earth System Science. Progress in Physical Geography, 33(6), 769–791.