## Slide 1: Teaching about Measuring Water Resources with GPS, Gravity, and Traditional Methods
Module authors: Bruce Douglas (Indiana University) and Eric Small (University of Colorado) Editor: Beth Pratt-Sitaula (UNAVCO)

## Slide 2: Technology
Please stay muted when you are not talking
Best to use earphones
Please make sure your real name shows in the Zoom Participant list
Use chat box a lot! (group or private messages)
Raise your hand if you have something more complicated so we can call on you. Then you can unmute to speak.
We will not be recording the session, but will save the chat.
In breakout groups it is best to turn on videos to facilitate interactions (internet withstanding).
Closed captions are available in main Zoom room (if you depend on closed captions, please private-message “UNAVCO host” so you can be put in a breakout group that stays in the main room)
Poll #1
Notes: 1. What is the primary course are you anticipating teaching these module materials in? ( Single Choice)
Answer 1: Hydrogeology (majors-level)
Answer 2: Hydrology (majors-level)
Answer 3: Physical geology (majors-level)
Answer 4: Environmental science/geology (majors-level)
Answer 5: Introductory earth science (all types of intro courses)
Answer 6: Other - put course name in chat
2. How long have you taught water resources/hydrogeology topics? ( Single Choice)
Answer 1: More than 10 years
Answer 2: 2-9 years
Answer 3: Less than 2 years (including I haven't taught yet)

## Slide 3: Water resource monitoring GEODETIC & TRADITIONAL METHODS

## Slide 4: High Precision vertical GPs

## Slide 5: What Is GPS?
GPS receivers are in phones, cars, etc.—basically anything that tells you where you are
This is a great entry point for engaging students
Note: GPS is the USA’s system
GNSS = global navigation satellite system (all systems)
Notes: Whether they know it or not, students use GPS receivers daily in their cars, phones, cameras, and handheld recreational GPS. Most have heard the term “GPS,” but few know much about how the system actually works or high-precision GPS for science and industrial use.
Note: Although the term GPS (Global Positioning System) is more commonly used in everyday language, it officially refers only to the USA's constellation of satellites. GNSS (Global Navigation Satellite System) is a universal term that refers to all satellite navigation systems including those from the USA (GPS), Russia (GLONASS), European Union (Galileo), China (BeiDou), and others. In this module, we use the term GPS even though, technically, some of the data may be coming from satellites in other systems.
Images from UNAVCO

## Slide 6: How actual location is determined
Antenna position is determined by calculating the distances to at least 4 satellites. This enables the solving for four variables: x, y, z and time using trilateration.
http://spaceplace.nasa.gov/gps-pizza/en/
Notes: The time element is needed because of the difference between the highly accurate atomic clock on the satellites ($100,000 each) and the much-cheaper clock in the GPS receivers.
Although 4 is a technical minimum number of satellites, for geoscience research work it is highly recommended to have at least 6 satellites.
Although people will often refer to this process and “triangulation” in fact it is “trilateration” because it depends on distances rather than angles.
For a nice explanation of trilateration versus triangulation visit https://gisgeography.com/trilateration-triangulation-gps/.
Images from NASA (public domain) http://spaceplace.nasa.gov/gps-pizza/en/

## Slide 7: Consumer-grade GPS accuracy
Horizontal: ~ 10 m error
Vertical: ~ 15 m error
Your location is:
37o 23.323’ N
122o 02.162’ W
Notes: Since each satellite maintains time very accurately (~1 nanosecond = 30 cm), it can tag its signal with the time of transmission. This information, together with the location of the satellite, also transmitted to the receiver, is sufficient to allow the receiver to calculate the range to each satellite provided that the receiver also knows also knows the time. Equipping receivers with atomic clocks would be very expensive, so the receiver tags the signal with the time of its internal clock to create a “pseudorange” (range plus an unknown clock correction). The software in the receiver than uses the pseudoranges from four satellites to solve for the four unknowns: three coordinates and the receiver clock correction.
Image by Vince Cronin (Baylor University)

## Slide 8: High-precision Permanent GPS Station
GPS antenna inside of dome
Monument solidly attached into the ground with braces.
If the ground moves, the station moves.
Solar panel for power
Equipment enclosure
GPS receiver
Power/batteries
Communications/ radio/ modem
Data storage/ memory
Errors after 24 hours:
Horizontal: ~1-2 mm error Vertical: ~ 5 mm error
Velocities after year or two: 1-2 mm/yr
Notes: Example of a typical remote GPS station. In urban areas, some are also fixed to the roof of large reinforced buildings and hooked into grid power supply with battery backup. Many stations are now being equipped with “real time” communication to allow immediate transfer of data to researchers. In other places logistics or country-specific regulations require that data not be transmitted but is instead downloaded manually on a given schedule (monthly, quarterly, annually depending on the site)
Accuracies are a little complicated because it does depend on the length of observation time. Nevertheless, this general guideline from the GAMIT/GLOBK 10.6 release notes is helpful. "With 24-hr sessions and a robust stabilization, obtained uncertainties and repeatabilities should be at the level of 1-2 mm for horizontal coordinates and 3-5 mm for heights. With 8-hr sessions, the horizontal should be 2-4 mm and height 10-15 mm.”
Generally robust velocities of as little as 1-2 mm/yr can be determine after a year or two.
Image from UNAVCO

## Slide 9: GPS Networks
Thousands of stations across continental United States
Data latency of ~1 day
http://geodesy.unr.edu/NGLStationPages/gpsnetmap/GPSNetMap.html
Notes: GPS stations are widely distributed around the USA and most data are available with a day or so. Some are available with seconds.
Image from Nevada Geodetic Laboratory (http://geodesy.unr.edu/sitemap.php) and used with permission. Base map by Google Maps.

## Slide 10: GPS Vertical Position
The solid Earth responds elastically to changes in load, such as water loss from regional groundwater pumping or drought
instantaneous, reversible, linear
Plate Boundary Observatory station P037
Notes: This is not the same as the isostatic adjustment to surface loads (long time scale, spatial pattern affected by flexural characteristics of lithosphere, total magnitude depending on crust/mantle density contrast).
The reverse also happens: add groundwater, TWS increases, the land surface moves down
Image from UNAVCO (http://www.unavco.org/instrumentation/networks/status/pbo/overview/P037)

## Slide 11: GPS Data
Cycles in vertical position are related to the seasonal water changes.
Notes: GPS stations such as those in the *Network of the Americas (NOTA; https://www.unavco.org/instrumentation/networks/status/all) were originally installed to measure things such as plate tectonic motion (horizontal motions shown in the left image). However, as the data came in, it became clear that elements of the vertical motion is related to changes in the terrestrial water storage (TWS) and there were much wider uses for GPS data than originally imagined.
* Many of these GPS stations were originally installed as part of the Plate Boundary Observatory (PBO), which was absorbed into NOTA in 2018.
Rear image: UNAVCO Velocity Viewer http://www.unavco.org/software/visualization/GPS-Velocity-Viewer/GPS-Velocity-Viewer.html (base image from Google Maps)
GPS and GPS data from https://www.unavco.org/instrumentation/networks/status/nota/overview/CABL

## Slide 12: Reflection GPS for snow depth

## Slide 13: Using GPS-Reflectometry for terrestrial hydrology studies
Changes in the ground such as added snow change the path and characteristics of the reflect GPS signal
P101 (Utah)
Notes: GPS stations were originally installed to measure tectonic motions. Position is determined by calculating the distances from satellites using the direct incoming signals. Originally all signals that reflected off surrounding surfaces were considered noise and researchers did their best to filter them out. However, more recently researchers at the University of Colorado Boulder realized that the the reflected signal could be used to determine things such as changes in height or conditions of the surrounding ground.
Image from UNAVCOO.

## Slide 14: Reflected GPS Signals

## Slide 15: GPS reflection footprint: ~1000 m2 Measurement frequency: daily
Meters
Meters
GPS
Notes: Unlike a SNOTEL pillow which only measures a few square meters of area, reflected GPS signals integrate snow depth from an around of about 1000 sq meters.
Image from Eric Small.

## Slide 16
Choosing sites for terrestrial hydrologic variables
P013, Paradise Valley, NV
P015, Show Low, AZ
BAD: Buildings, roads, complex topography, cows
Good: natural ecosystems, undisturb-ed surface, simple topography
Notes: red = right hand
blue = left hand
antenna is L2 Choke antenna

## Slide 17: GRACE Missions: Gravity Recovery and Climate Experiment
Original GRACE satellites 2002-17
GRACE Follow-on launched 2018
Notes: http://photojournal.jpl.nasa.gov/jpegMod/PIA04235_modest.jpg (public domain)
https://gracefo.jpl.nasa.gov/resources/71/grace-fo-mission-brochure/

## Slide 18: How GRACE Measures Gravity
Notes: This graphic from NASA is specifically illustrating the Caribbean Sea, Colombia, and Peru but can be used as a general explanation of how GRACE measures gravity. From https://gracefo.jpl.nasa.gov/resources/50/how-grace-fo-measures-gravity/ A simplified example of how the distance between the GRACE-FO satellites changes as they pass over areas with lower mass (example: the ocean) and areas with higher masses (example: land.)
Panel 1: When both spacecraft are over the ocean, the distance between them is relatively constant.
Panel 2: When the leading spacecraft encounters a more massive object (in this case, land), the more massive area’s higher gravity pulls it away from the trailing spacecraft, which is still over the less massive area.
Panel 3: Once the second satellite also encounters the more massive area, it too is pulled toward the higher mass and consequently toward the leading spacecraft. As the lead spacecraft moves past the more massive area, it is pulled back slightly by the higher gravity of that area.
Panel 4: When both spacecraft are over the less massive object (in this case, the ocean) again, the trailing spacecraft is slowed by land before returning to its original distance behind the leading spacecraft.

## Slide 19: Example of distance & topography relationship
Notes: OPTIONAL
https://gracefo.jpl.nasa.gov/news/138/first-laser-light-for-grace-follow-on/
“Along the satellites' ground track (top), the inter-spacecraft distance between them changes as the mass distribution underneath (i.e., from mountains, etc.) varies. The small changes measured by the Laser Ranging Interferometer (middle) agree well with topographic features along the orbit (bottom).”
This may be more information that you wish to get into with students but in reality there is a somewhat complex relationship between the distance between the satellites and the underlying topography/gravity with oscillations that need to be converted into a gravity value.

## Slide 20: GRACE data characteristics:
2-6 month latency (or more)
Monthly data (some months missing)
Coarse spatial resolution (~100 km)
GRACE original mission ran 2002-2017 (5-year expected duration was far outlived but by late 2016 GRACE was under modified operations to prolong battery life)
GRACE Follow-on mission launched May 2018. Education-ready data still in process.

## Slide 21: Example of GRACE Groundwater Data
Notes: A decade of GRACE data shows the overall changes in aquifers across the USA.
Image from: https://earthobservatory.nasa.gov/IOTD/view.php?id=82266
NASA site also includes a related article which instructors could use to bring in more aspects of specific societal challenges from groundwater loss.

## Slide 22: GRACE April 2015 anomaly from 2002-2015 average
Notes: The gravity variations measured by GRACE can be used to determine water storage on land. By comparing current data to an average over time, scientists can generate an anomaly map to see where terrestrial water storage has decreased or increased. This map, created using GRACE data, shows the global terrestrial water storage anomaly in April 2015, relative to the 2002-2015 mean. Rust colored areas show areas where water has decreased, and areas in blue are where water levels have increased. Note the significant decreases in water storage across most of California are related to groundwater, while decreases along the Alaska coastline are due to glacier melt.
https://gracefo.jpl.nasa.gov/resources/71/grace-fo-mission-brochure/

## Slide 23: Traditional Methods Also Included
SNOTEL – snow pillows
Stream gauges
Groundwater
wells

## Slide 25: Measuring Water Resources
3/31/2011
3/31/2015
Notes: Satellite images of the snow pack in the Sierra Nevada Mountains in March 31, 2011 and 2015.
2015 was the depths of the exceptional drought that California experienced.
http://earthobservatory.nasa.gov/IOTD/view.php?id=86838&src=eoa-iotd

## Slide 29: Unit 1 Outline
Hydrologic cycle – reservoirs, fluxes, and resident time
Traditional hydrologic measurements
  Stream Gauging stations
  SNOTEL stations (snow mass)
  Groundwater wells
  Rainfall
Introduction to geodesy and geodetic water measurement methods
Stakeholder Analysis

## Slide 30: Annual Hydrological Cycle
Cockell, 2008 Fig. 1-38
Notes: Many assumptions go into determining these fluxes and reservoir masses. Although other studies may give somewhat different numbers, the overall scale of the different residence times gives students a reasonable idea of where water resides for mere days-weeks or millennia. For simplicity, not all fluxes are included.
Fluxes and reservoir masses taken from: Oki & Kanae, 2006. Global hydrologic cycles and world water resources. Science, v 303, p 1068-1072. http://science.sciencemag.org/content/sci/313/5790/1068.full.pdf?ijkey=5C.sNh5aehB66&keytype=ref&siteid=sci.pdf
Background image: http://www.noaa.gov/resource-collections/water-cycle

## Slide 31: Humans are part of the water cycle
What reservoirs and transport paths are most affected by human activity?
Notes: Human influence on the hydrologic cycle is frequently left off of water cycle diagrams. Engage your students in a short brainstorm on ways that humans influence the water cycle.

## Slide 32: Valuable resource for reference and reading
Notes: https://pubs.er.usgs.gov/publication/cir1441

## Slide 33
Potential Stakeholders
Public Water Supply
Heavy Industrial Use
Agricultural Use
Environmental Needs
Recreation + Entertainment
Governmental Officials
Environmental Organizations
Unit 1 exercises starts with students brainstorming water resources stakeholders such as these
Notes: https://pubs.er.usgs.gov/publication/cir1441

## Slide 34: Methods for Categorizing Stakeholders
Example Stakeholder Cross Plot of Interest vs. Power/Influence.
Example Stakeholder Concept Diagram
Notes: Figure 1. Example of a graphic depiction of where various stakeholders sit with regards to two specific qualities that enter into a Stakeholder relationship – Power and Interest. Other plots relating other stakeholder variables can be made in a similar fashion
http://www.stakeholdermap.com/stakeholder-analysis.html

## Slide 35: Breakout #1 (15 minutes)
Part of Unit 1 student exercise related to conducting a stakeholder analysis
Each breakout group will have a Google Slides file
You will fill in stakeholder Power vs Interest chart
  Thinking and talking about how this might work in your online and/or face-to-face class
Whole-group report out: each group will have 2 minutes to share a thought on teaching or screen share chart

## Slide 37: Measuring Water Resources
Unit 2: Characterizing groundwater storage with well and GRACE data
Notes: Left image: http://photojournal.jpl.nasa.gov/jpegMod/PIA04235_modest.jpg

## Slide 38: Unit 2 Outline
Terrestrial Water Storage (TWS) defined
Relationship between TWS and groundwater storage
Traditional measurement: Groundwater wells
  Depth to water table and groundwater storage
Geodetic measurement: GRACE (Gravity Recovery and Climate Experiment) satellite
  Uses gravity to measure changes in mass

## Slide 39: Groundwater Record

## Slide 40: Geodesy & Hydrology
Satellite gravity measurements (GRACE – Gravity Recovery and Climate Experiment)
  Changes is gravity can show groundwater changes
climate.nasa.gov
Notes: The GRACE satellite

## Slide 41: GRACE Record

## Slide 43: Measuring Water Resources
Unit 3: Monitoring groundwater storage with GPS vertical position
Notes: Plate Boundary Observatory station P422 in Moscow Idaho
Image from UNAVCO http://www.unavco.org/instrumentation/networks/status/pbo/overview/p422

## Slide 44: Unit 3 Outline
Groundwater Mining: a Global Problem
GPS vertical position and hydrologic loading
Subsidence: compaction and poroelastic effects
Introduction to California physiography

## Slide 45: 1. Groundwater mining: a global problem
These figures are from Konikow, 2011
See also Figure 2 from Famiglietti, 2014
Konikow, Geophysical Res. Letters, 2011
NASA EarthObservatory
Notes: A variety of water measurement methods show that groundwater aquifers from around the world are being depleted.
The left image from Konikow, 2011, (http://onlinelibrary.wiley.com/doi/10.1029/2011GL048604/abstract) was derived from a wide range of methods including water level, modeling, and pumpage.
The right image from NASA (also detailed in Famiglietti, 2014) was based on GRACE data (Gravity Recovery and Climate Experiment).
Left image: Konikow, 2011 – AGU journals allows use of published image for educational purposes
Right image: https://earthobservatory.nasa.gov/blogs/earthmatters/2014/11/05/earths-disapearing-groundwater/ (J.T. Reager, NASA Jet Propulsion Laboratory)

## Slide 47: GPS Data
Cycles in vertical position are related to the seasonal water changes.
Notes: GPS stations such as those in the *Network of the Americas (NOTA; https://www.unavco.org/instrumentation/networks/status/all) were originally installed to measure things such as plate tectonic motion (horizontal motions shown in the left image). However, as the data came in, it became clear that elements of the vertical motion is related to changes in the terrestrial water storage (TWS) and there were much wider uses for GPS data than originally imagined.
* Many of these GPS stations were originally installed as part of the Plate Boundary Observatory (PBO), which was absorbed into NOTA in 2018.
Rear image: UNAVCO Velocity Viewer http://www.unavco.org/software/visualization/GPS-Velocity-Viewer/GPS-Velocity-Viewer.html (base image from Google Maps)
GPS and GPS data from https://www.unavco.org/instrumentation/networks/status/nota/overview/CABL

## Slide 48: 3. Subsidence: groundwater pumping may lead to subsidence
Two effects
  Compaction of aquitard sediments; generally irreversible
  Poroelastic effects; reversible

## Slide 49
http://pubs.usgs.gov/circ/circ1182/pdf/04part1_intro.pdf

## Slide 50
http://pubs.usgs.gov/circ/circ1182/pdf/04part1_intro.pdf

## Slide 51: Instructions to the students
 | Station | Latitude | Longitude | Vertical Trend (mm / yr) | Month of peak in seasonal cycle
Person 1 | P536 | 35.28 | -120.03 |  | 
 | P056 | 36.03 | -119.06 |  | 
 | P567 | 35.42 | -118.75 |  | 
Person 2 | P538 | 35.53 | -120.11 |  | 
 | P303 | 37.05 | -120.71 |  | 
 | P570 | 35.67 | -118.26 |  | 
Person 3 | P539 | 35.70 | -120.18 |  | 
 | P307 | 36.95 | -120.06 |  | 
 | P572 | 36.59 | -118.95 |  | 
II. The Data
GPS records from nine GPS stations are provided (Table 1). You will work in a group of three – each of you will analyze data from three of the sites and share their results with others in the group. The GPS sites are split into three groups for you. Each person should select one group and proceed.
Table 1. Station name and location for nine PBO sites in California. Answers for vertical trend and timing of peak in seasonal cycle should be inserted into this table as you arrive at the answers working through exercise’s questions.

## Slide 53
4-character names are station ID

## Slide 54: Time to Work with GPS data for Unit 3
unit_3_instructor_data-shortcourse.xlsx

## Slide 55: Breakout #2 (20 minutes)
This activity is from Measuring Water Resources with GPS, Gravity, and Traditional Methods module Unit 3: Monitoring groundwater storage with GPS vertical position student data exercise (subset).
Open the file unit_3_instructor_data-shortcourse.xlsx
  There are 9 stations of data
  Normally each team would have 3 students, who each look at 3 stations each Today we are suggesting that ~2 of you work on each of station set-of-3
Work through the questions on the slides

## Slide 56
Rapid downward movement
Stations on sedimentary basin
Slow uplift
Stations on bedrock

## Slide 57
GETSI modules have answer keys in a protected “teacher stash” available to identified instructors

## Slide 58
Notes: https://www.youtube.com/watch?v=5Bzt374u5aU&index=2&list=PLzmugeDoplFOot41MIBBZiLYBCB0M-p1P&t=6s

## Slide 59: Thoughts and Ideas
Poll #2
What thoughts did you have during the exercise?
  Ideas for implementing?
  Perceived challenges/hurdles?
Fine to raise your hand and we’ll call on you to unmute and speak.
Chat box also great to use.
Notes: https://www.youtube.com/watch?v=5Bzt374u5aU&index=2&list=PLzmugeDoplFOot41MIBBZiLYBCB0M-p1P&t=6s
Poll #2
Do you see yourself using the "GPS & Groundwater" animation before or after the data exercise? (feel free to add explanation into the chat box) ( Single Choice)
Answer 1: Before (ex. to set up students with some base knowledge for analyzing GPS data)
Answer 2: After (ex. do not want to give students clues to the data analysis "answer" beforehand, so animation could serve as wrap-up visualization of what they saw in the data)

## Slide 62: Measuring Water Resources
Unit 4 Water budget assessment of a California drought
Notes: Image: California Department of Water Resources

## Slide 63: Unit 4 Outline
CA drought: Spatial extent, timing, and historical perspective
California Physiography: Mountains and valley
Drought and societal impacts
Precipitation record
Measuring snow with SNOTEL snow pillows and GPS-IR
GRACE data set as well as kmz overlays for Google Earth
Executive Summary Report

## Slide 66: SNOTEL stations
Weight of snow on the pillow allows measurement of contained water mass
Snow Water Equivalent (SWE) is the depth of water that would result if all the snow was melted.
Pressure from the overlying snow is measured beneath the pillow. Information is transmitted to data centers.
Notes: SNOTEL stations are very valuable, but they provide only a point source of information. Snow depth is notoriously variable due to factors such as wind and vegetation. It is not feasible to have the density of these stations that would really help constrain snow mass more comprehensively. Also the measurements are only over an area of a few square meters for each site. Geodetic methods such as reflection GPS can help augment data from SNOTEL stations.
SNOTEL stations contain a variety of equipment.
The primary measurement is determination of snow mass through the pressure sensor within the pillow.
Other equipment collects snow depth (look-down sensor) and a variety of other meteorological equipment.
Image: https://www.nrcs.usda.gov/wps/portal/nrcs/detail/id/snow/?cid=nrcs144p2_047776

## Slide 67
SNOTEL
April 2014

## Slide 68
SNOTEL
April 2015

## Slide 71
2011

## Slide 72
2014

## Slide 73
2011 – 2014
Difference

## Slide 74: Implementation Planning-Exploring-Feedback
Spend the remaining time of the mini-course working on implementation planning
  Explore other aspects of the module or GETSI
  Write down steps you need to do to get ready to teach with this module
  Fill out form: link posted in the chat Complete by Sunday Nov 8 for stipend eligibility*
Intro-level water resources module Eyes on the Hydrosphere: Tracking Water Resources
*US Citizens and residents only for stipend. Stipends will be compiled after the end of the term and sent together. But the implementation plan is useful to all participants!

## Slide 75: Upcoming GETSI Mini Courses
Teaching in the Field about High Precision Positioning with Static and Kinematic GPS/GNSS [Majors-level module]
  Date: Tuesday November 17, 2020
  Time: 12-2 pm PT | 1-3 pm MT | 2-4 pm CT | 3-5 pm ET | 7-9 pm UTC
  Registration deadline: Sunday November 15, 2020 - registration form opening soon
More mini-courses are expected in early 2021
If you use a GETSI module in your teaching, please fill out a “Share Your Experience” survey afterwards ($100 stipend).