## Slide 1: ENEC Lecture 17: Floods
Yukon River - Alaska, 2013
25km
NASA MODIS Satellite Imagery
Notes: More information about the 2013 Flooding
Galena, Alaska, residents evacuate when ice dam causes major flooding - CBS News

## Slide 2: Day 1 Learning Goals
Calculate flood recurrence intervals and exceedance probabilities
Define hazard, vulnerability, and risk
Interpret spatial patterns in flood hazard and vulnerability maps
Describe different ways in which flood hazard and risk can be mitigated
Understand the format and requirements of the upcoming role-playing activity

## Slide 3
Global flood hazard
Floods are the most deadly natural disasters worldwide.
Over the period of 1980-2009 ~500-600k people died in floods
Over the same period approximately 2.8 billion people were affected by floods
Citation: Doocy et al, PLOS, 2013
Above: Landsat imagery from August 2022 of large-scale flooding in northern Pakistan (courtesy of NASA)
Link: Dr. Shannon Doocy, Johns Hopkins

## Slide 4
Natural Hazard: Physical process which has the potential to cause loss or damage to something valued by an individual or a society.
Human impact
What causes flooding?
Figure from Brand et al. (2017)
Notes: Ask students what might cause flooding. Write student answers on the board.

## Slide 5
Natural Hazard: Physical process which has the potential to cause loss or damage to something valued by an individual or a society.
Human impact
How might humans impact flood hazard?
Figure from Brand et al. (2017)
Notes: Ask students how humans might impact flood hazard – write responses on the board.

## Slide 6: Key Point
Floods often happen naturally, but flood hazard represents a complex interplay between natural processes and human landscapes and decisions.
To understand floods, we need to think about both human and nonhuman factors.

## Slide 7: Cascading hazards
“Cascading disasters are extreme events, in which cascading effects increase in progression over time and generate unexpected secondary events of strong impact.” -Pescaroli & Alexander (2015)

## Slide 8: Cascading hazards
Other Examples
Hurricane → Dam Failure/Flood→ Disease/Famine
“Cascading disasters are extreme events, in which cascading effects increase in progression over time and generate unexpected secondary events of strong impact.” -Pescaroli & Alexander (2015)

## Slide 9: Links w/ additional reading
Ice Jam Flooding: Galena, Alaska, 2013-link 1 & link 2
Coastal Hurricane Flooding: Hurricane Katrina, 2005 - link
Landslide-driven: Uttarakhand flood, 2021 - link
General riverine: Great Mississippi Flood of 2011 - link
Dam failure/Typhoon: Banqiao Dam Failure, 1975 - link

## Slide 10
Vulnerability: Potential for damage or loss of a social or economic asset.
Human impact
Human impact
What impacts vulnerability?
Figure from Brand et al. (2017)

## Slide 11
Vulnerability: Potential for damage or loss of a societal asset.
figure from Geography.org.uk
Link to classification of indicators
Notes: Exposure An area’s predisposition to disruption by a Exposure can be understood as the geographical flooding event due to its location in the same characteristics that are present at the place area of influence. where floods can occur. These characteristics may be infrastructure, cultural heritage, land use, people etc. The indicators for this component can be separated into two categories: the first one covers the exposure of different elements at risk; the second includes details on the general characteristics of the flood.
Susceptibility The elements exposed within the system Susceptibility relates to system characteristics, (e.g. people, property, infrastructure etc.) including the social context of flood damage which influence the probabilities of being occurrence – especially the awareness and harmed at times of hazardous floods. preparedness of affected people (before the flood) regarding the risk they live with, the institutions that are involved in mitigating and reducing the effects of the hazards, and the existence of possible measures such as evacuation routes to be used during the floods.
Resilience The capacity of a system to endure a Resilience to flood damage can be evaluated only hazard/disaster event such as a flood, in places which have experienced past events, maintaining significant levels of organisation since the main focus is on the experiences in its social, economical, environmental and encountered during and after the floods.

## Slide 12
With your neighbors, list two things that would impact each of the components of vulnerability?

## Slide 13
Risk: Likelihood of asset damage or loss due to an extreme event.
Human impact
Figure from Brand et al. (2017)

## Slide 14: Flood frequency analysis
The objective of flood frequency analysis is to relate the magnitude of events to their frequency of occurrence through a probability distribution
The magnitude of extreme events is related to their frequency of occurrence
We can define floods by their recurrence interval. For example, a 100-year flood is the largest flood that occurs, on average, every 100 years
It is assumed that all flood events are independent
Why should you care? Flood frequency is often how we inform flood insurance, decide on flood mitigation, and also inform home purchasing/lending.
Notes: https://riskfactor.com/property/228-butler-ct-nc/371381787_fsid/flood

## Slide 15: Return period / recurrence interval
R(x) = recurrence interval of a
flood with a magnitude X
n = number of years of record
m = rank of event - ranking from largest to smallest
Year | Max discharge (cfs) | Rank
2010 | 13500 | ?
2011 | 15700 | ?
2012 | 8200 | ?
2013 | 6800 | ?
2014 | 28100 | ?
2015 | 23600 | ?
2016 | 31600 | ?
What is the return period of a 28,100 cfs (cubic feet per second) flood?
Definition: On average, how often would you expect a flood of magnitude X to occur?

## Slide 16: Return period / recurrence interval
R(x) = recurrence interval of a
flood with a magnitude X
n = number of years of record
m = rank of event - ranking from largest to smallest
Year | Max discharge (cfs) | Rank
2010 | 13500 | 5
2011 | 15700 | 4
2012 | 8200 | 6
2013 | 6800 | 7
2014 | 28100 | 2
2015 | 23600 | 3
2016 | 31600 | 1
What is the return period of a 28,100 cfs (cubic feet per second) flood?
Definition: On average, how often would you expect a flood of magnitude X to occur?
R(28,100) = (7+1)/2 = 4 years

## Slide 17: Yearly exceedance probability
Definition: In a single year, how likely is it for a flood of X magnitude to occur?
OR
P(X) = Probability of exceeding a flood of magnitude X in a single year
m = rank of event
n = number of years of record
R = recurrence interval

## Slide 18: Yearly exceedance probability
OR
P(X) = Probability of exceeding a flood
of magnitude X in a single year
m = rank of event
n = number of datapoints
R = recurrence interval
Year | Max discharge (cfs) | Rank
2010 | 13500 | 5
2011 | 15700 | 4
2012 | 8200 | 6
2013 | 6800 | 7
2014 | 28100 | 2
2015 | 23600 | 3
2016 | 31600 | 1
What is the yearly exceedance probability of a flood with a magnitude of 28,100 cfs

## Slide 19: Yearly exceedance probability
OR
P(X) = Probability of exceeding a flood
of magnitude X in a single year
m = rank of event
n = number of datapoints
R = recurrence interval
Year | Max discharge (cfs) | Rank
2010 | 13500 | 5
2011 | 15700 | 4
2012 | 8200 | 6
2013 | 6800 | 7
2014 | 28100 | 2
2015 | 23600 | 3
2016 | 31600 | 1
What is the yearly exceedance probability of a flood with a magnitude of 28,100 cfs
¼ or 0.25

## Slide 20: Exceedance Probability
In a period of y years, what is the likelihood of a flood of magnitude X occurring?
P(x) = probability of a flood of X magnitude occurring in y years
R = recurrence interval
y = number of years of concern

## Slide 21: Exceedance Probability
P(x) = probability of a flood of X magnitude
occurring in y years
R = recurrence interval
y = number of years of concern
Year | Max discharge (cfs) | Rank
2010 | 13500 | 5
2011 | 15700 | 4
2012 | 8200 | 6
2013 | 6800 | 7
2014 | 28100 | 2
2015 | 23600 | 3
2016 | 31600 | 1
What is the probability of a flood of magnitude 28,100 cfs occurring within a 3 year period?

## Slide 22: Exceedance Probability
P(x) = probability of a flood of X magnitude
occurring in y years
R = recurrence interval
y = number of years of concern
Year | Max discharge (cfs) | Rank
2010 | 13500 | 5
2011 | 15700 | 4
2012 | 8200 | 6
2013 | 6800 | 7
2014 | 28100 | 2
2015 | 23600 | 3
2016 | 31600 | 1
What is the probability of a flood of magnitude 28,100 cfs occurring within a 3 year period?
1-(1-(¼))^3 = 0.58 or 58% chance of occurrence in 3 years

## Slide 23
By conducting statistical analysis of discharge over a long period of time, we can define recurrence intervals for floods of different sizes (e.g. the 1-year, 10-year, or 100-year flood).
Discharge (ft3/sec or cfs)
Recurrence interval (years)
“What is the magnitude of a 100-year flood?”

## Slide 24
What other assumptions are we making that might impact the accuracy of our flood frequency analysis calculations?

## Slide 25
Time to put on our engineering caps...
Photo: Tomorrow’s Engineers Week
Photo: Schexnaydre Construction

## Slide 26
Flood risk can be mitigated by reducing the hazard or its consequences, where consequences are a function of exposure, vulnerability and resilience.
Flood mitigation includes any measure intended to reduce flood risk.
Structural or non-structural
Parcel-scale or Community-scale

## Slide 27
Image Source: BBC, Channel Modifications
Structural
Google Maps Street View, near Houma LA of Home Elevation
Physical modifications to structures, infrastructure, and landscape

## Slide 28
FEMA National Flood Insurance Program
Non-Structural
Disaster loan programs
Programs and policies that reduce the consequences of hazards

## Slide 29
Flood risk can be mitigated by reducing the hazard or its consequences, where consequences are a function of exposure, vulnerability and resilience.
Flood mitigation includes any measure intended to reduce flood risk.
Structural or non-structural
Parcel-scale or Community-scale
Community Scale
Parcel Scale

## Slide 30
 | Structural | Non-structural
Parcel-scale | Elevating structures Sump pumps & sand bags | Purchasing flood insurance or receiving a flood loan Moving away or participating in a buyout program
Community-scale | Levees Detention/Retention Ponds | Offering buyouts Offering a flood insurance or flood loan program
Of these categories:
Which takes the longest to implement?
Which costs the most to individual people?
Are there any mitigation strategies that might impact social support networks?

## Slide 31
Other questions to assess mitigation strategies
Who has to pay for the mitigation? Are there resources to help pay for a mitigation?
How long does it take to implement the mitigation?
How long will the mitigation last due to climate change and urbanization?
How many people and who will benefit from the mitigation?
How will the mitigation impact the environment?
Could the mitigation increase flood hazard/risk if it fails?

## Slide 32
Direction of water flow

## Slide 33
Juan et al. (2020)
1950s & 60s
Army Corps of Engineers deepened & widened Brays Bayou and lined it with concrete (aka channelization)

## Slide 34
Increasing discharge caused by urbanization and ‘channelization’
USGS Gage Data
Source: USGS

## Slide 35
Image from the Harris County Flood Control District
Notes: TLDR: Allison stalled out over the Houston Metro Area as a Tropical Storm, causing a ton of rainfall!

## Slide 36
Flood maps modified from the Tropical Storm Allison Recovery Project (TSARP.org) a partnership between FEMA and the HCFCD. Link to original images.

## Slide 37
Brays Bayou Flooding During Tropical Storm Allison
Thanks to Dr. Antonia Sebastian for the modeled flood data

## Slide 38: This is where you come in…
You are one of the following:
Neighborhood resident (Braeswood Place, Magnolia Park, Willow Meadows/Meyerland)
Texas Medical Center Representative
Government employee (Houston County Flood Control District, City of Houston)
Environmental Activist (Texas Living Waters Project)
You will be further divided up into subgroup 'A', 'B' or 'C', which will determine the mitigation strategies that you will read about and become an expert in...
Next week, there will be a community town hall, hosted by the Texas Living Waters Project, in which the community will come together to create and vote on a flood mitigation plan for Brays Bayou to prevent future flooding.

## Slide 39
The activity will be structured as follows
Meet with people of your role to discuss flood mitigation options that work best for your role (day 2)
    Subgroup meeting, role meeting
Split up into multiple town halls, in which each town hall has several people from each role, to develop and vote on the town’s flood mitigation strategy (day 3)
Finish up town halls & activity reflection (day 4)

## Slide 40: Deliverables
Homework due 11/10: Pre-Assignment (10 pts) - individual submission
  Based on your role and subgroup
In Class: Sub-group worksheet (25 pts) - one submission per sub-group
In Class: Whole-Role worksheet (20 pts) - one submission per role
In Class: Working Group Proposal Document (30 pts) - small group submission
In Class: Reflection Document (5 pts) - individual submission
Remember the Sakai checklist!

## Slide 41: Flood map data
Dark purple = deeper flood water
Light blue = shallower flood water
100-year flood, screenshot from FloodFactor.com (no longer online)
Notes: FloodFactor.com

## Slide 42: Flood map data
Note, the flood depth for the role-playing activity will look like this, below! It is actual modeled flood data from Tropical Storm Allison!
Data provided by Dr. Antonia Sebastian
Notes: FloodFactor.com

## Slide 43: Demographic data
Dark red =
High percentage of low-income population (relative to the nation as a whole)
Light gray =
Low percentage of low-income population (relative to the nation as a whole)
EPA: Environmental Justice Mapper
Notes: EPA: Environmental Justice Mapper
Low income = population whose income level is less than 2x the poverty level

## Slide 44: Environmental data
Dark red = Areas close to hazardous waste facilities (relative to the national average)
Light gray =
Areas far away from hazardous waste facilities (relative to the national average)
EPA: Environmental Justice Mapper
Notes: EPA: Environmental Justice Mapper
Proximity = Count of waste transfer, storage and facilities divided by the distance to the location

## Slide 45
Deeper Water
Deeper Water
Shallower Water
100-year flood
Low-income population
More low-income population
Less low-income population
Hazardous Waste Proximity
Closer to hazardous waste
Further from hazardous waste
What is the spatial relationship between flooding and low-income population?
Where might be the highest risk for flooding-driven cascading hazards?

## Slide 46: Bonus unused slides w/ a few more examples of hazard vs risk
All block model images in the following slides were generated by Dr. Dolan

## Slide 47
What is the hazard in this situation? Is it the same on both sides of the river?
Which side of the river has higher risk?
Notes: Instructor goes over an example of classifying the flood/hazard/risk in this scenario

## Slide 48
What is the hazard in this situation? Is it the same on both sides of the river?
The flood water – extent, height, duration, same on both sides
Which side of the river has higher risk?
Humans built a structure on the right side that is vulnerable to damage
Notes: Instructor goes over an example of classifying the flood/hazard/risk in this scenario

## Slide 49
Did humans increase and/or decrease hazard in this situation? If so, how?
Which side has increased risk?
Notes: Now, the students get to try on their own!
Answer:
Humans impacted hazard by building the levee
Left side probably has higher vulnerability (weren’t able to fight the fact that the levee was built on the other side)
The left side has the greater risk because it definitely has higher hazard due to flood waters and may also have higher vulnerability.

## Slide 50
Did humans increase and/or decrease hazard in this situation? If so, how?
Increased on the left and decreased on the right
Which side has increased risk?
Left side
Could the left side also be more vulnerable?
Notes: Now, the students get to try on their own!
Answer:
Humans impacted hazard by building the levee
Left side probably has higher vulnerability (weren’t able to fight the fact that the levee was built on the other side)
The left side has the greater risk because it definitely has higher hazard due to flood waters and may also have higher vulnerability.

## Slide 51
If this river were to flood, how would water height compare between the right and left sides of the river?
What features of the natural or built landscape explain your answer?
Which side has higher hazard?
Which side has higher risk?
Notes: Answer:
We would expect the water to be higher on the left-hand side of the river because it is a parking lot, so there can’t be any infiltration. Whereas on the right-hand side, there is regular grass, which allows for infiltration as well as the plants along the edge of the river which help to slow flow and trap sediment.

## Slide 52
If this river were to flood, how would water height compare between the right and left sides of the river? - higher on the left
What features of the natural or built landscape explain your answer? Parking lot on one side (impervious), vegetation (pervious and slows flow) on other
Which side has higher hazard? - Left
Which side has higher risk? - Left